## Slide 1: Introduction to the Contaminant Transport Module

## Slide 2: GoldSim and the Contaminant Transport Module
  The basic GoldSim framework consists of a flexible set of tools for creating dynamic, probabilistic simulations of nearly any kind of complex system.
    These tools are very abstract (like a programming language).
    They simply carry out mathematical calculations (e.g., numerical integration) that are applicable to many types of problems.
  In order to simulate some kinds of complex systems, such tools are not sufficient. Therefore, GoldSim has several specialized extension modules to facilitate simulation of some types of systems.
  The Contaminant Transport Module is a set of specialized elements that are added to GoldSim to support complex contaminant transport simulations.

## Slide 3: GoldSim and the Contaminant Transport Module
  The Contaminant Transport Module is powerful and complex.
  Today we will simply provide an overview.
  Due to the limited amount of time, will not work through examples together. Instead, I will simply present a number of examples.
  The Contaminant Transport Module is described in great detail in a free online course:

## Slide 4: GoldSim and the Contaminant Transport Module
  The module is used to simulate the movement of mass (typically contaminants) through natural (and engineered) systems.
  Produces predictions of mass transport rates at defined locations, concentrations in specified environmental media (e.g., water, soil), and impacts to defined human receptors (e.g., dose, health risk).
  Processes that can be simulated include mixing, solubility constraints, sorption, advection, dispersion, diffusion, and chemical reactions and radioactive decay and ingrowth.
  Can this be done with basic GoldSim?
    Simple mixing problems could be simulated, but any complex processes would be difficult or impossible to simulate without the Contaminant Transport Module.

## Slide 5: There are Two Contaminant Transport Module Versions
  CT and RT
  RT includes several specialized features primarily used to simulate the transport of radionuclides (e.g., simulation of decay chains)

## Slide 6: How Detailed and Highly Discretized Should Your Contaminant Transport Model Be?
Just because you can build a large, highly discretized model does not mean you should.
  How much uncertainty do you have in the source?
  How much uncertainty do you have in the key transport properties (e.g., partition coefficients, solubilities)?
  Do you really understand the dispersive characteristics of the system?
As a general rule, our ability to predict concentrations is much poorer (i.e., subject to greater uncertainty) than our ability to predict flows.

## Slide 7: Since all models are wrong the scientist cannot obtain a "correct" one by excessive elaboration… Just as the ability to devise simple but evocative models is the signature of the great scientist, so overelaboration and overparameterization is often the mark of mediocrity. George Box, Science and Statistics (1976)

## Slide 8: Top-Down Modeling

## Slide 9: Uranium Mine Closure

## Slide 10: Mine Water Treatment

## Slide 11: Shallow Radioactive Waste Disposal Facility

## Slide 12: Deep Radioactive Waste Disposal Facility

## Slide 13: Proposed Yucca Mountain Repository

## Slide 14: Contaminant Transport Module
Adds specialized elements to facilitate simulation of contaminant transport through engineered and natural environmental systems
r
RT Module Only

## Slide 15: Contaminant Transport Module
Provides a basic framework for modeling fate and transport of dissolved, sorbed and/or suspended contaminants through engineered and natural systems.
Complexity of the model is determined by the user.
While incorporating some basic physics (e.g., conservation of mass, decay and ingrowth, diffusion, partitioning), very few assumptions built into code in order to maximize flexibility.
Heavily utilizes arrays.

## Slide 16: Steps for Modeling Contaminant Transport
Specify species to be modeled.
Specify the transport and storage media within the system to be modeled (e.g., water, air, sediment, soil).
Specify the transport pathways through which mass is transported and stored.
Define the source terms (initial and/or boundary conditions).
Define the impacts of the species (e.g., dose) on defined receptors.

## Slide 17: Defining Species
Species element

## Slide 18: Environmental Media
Basic “building blocks” of transport pathways
  mass transport calculations are based largely on media properties
  Two types: Fluids and Solids

## Slide 19: Transport Pathways
Transport pathways represent those parts of the system through which species mass is transported and/or in which species mass is stored.
  Tanks, ponds, aquifers, lakes, soil columns, etc.
You define the properties of the pathways, such as geometry, volume, and pathway discretization.
You define which media (e.g., air, water, sediments, rock) types are present in the pathway.

## Slide 20: Transport Pathways
Pathways can be thought of as transfer functions.
Each pathway type (or transfer function) assumes or represents a particular range of physical transport processes.

## Slide 21: Transport Pathways
We will focus on Cells and Aquifers today.
GoldSim provides five type of pathways:

## Slide 22: Transport Pathways
You create a mass transport system by defining a network of transport pathways using mass flux links among the pathways.

## Slide 23: Pathways Mass Balance
Species mass is conserved.
The Contaminant Transport Module simulates mass transport so it solves for the mass of each species in each transport pathway.
  The water, or other media, balance is not a part of the transport module solution.
  Media advection rates are inputs (and not solution values) for transport pathways.
    You can link the transport media advection rates to a water balance model (or other media balance model) in order to enforce both a water balance and species mass balance.

## Slide 24: Contaminant Sources
You can specify initial and boundary conditions in Pathways.
In some cases, however, direct specification of an initial condition or rate of input is not possible. The RT Module allows you to simulate a source term using a Source element.
The Source element simulates:
  Failure of barriers containing the mass
  Degradation of matrix material (e.g., grout) in which the mass is bound
  Particularly useful when simulating engineered barrier systems
Won’t discuss further today.

## Slide 25: Receptors
The objective of many studies is not only to compute contaminant concentrations and fluxes at various locations, but to also compute the impact of these contaminants on specified receptors.
GoldSim provides a Receptor element that facilitates the conversion of contaminant concentrations in media within pathways to impact to defined receptors (e.g., dose, health risk).
Won’t discuss further today.

## Slide 26: Example1: Partitioning and Decay in a Cell
Assume 10 g of species C and D exists in Cell
The cell contains 10 m3 of Water and 10 kg of Sand
Sand has a dry density of 1600 kg/m3, and a porosity of 0.3
Partition coefficient for C in Sand: 2 m3/kg
Partition coefficient for D in Sand: 0 m3/kg
C decays with a half-life of 5 years
Run for 20 years

## Slide 27: Cell Pathways
Act as mixing cells
Can specify multiple media
Mass is instantly mixed and equilibrated (partitioned) within cell
Solubility constraints can be imposed in cell
Can have specified initial/boundary condition
Behavior of cell network is mathematically equivalent to network of finite difference nodes

## Slide 28: Equations Solved By GoldSim

## Slide 29: Example1a: Partitioning Decay and Ingrowth in a Cell
Assume C decays to D

## Slide 30: Equations Solved by GoldSim

## Slide 31: Mass Flux Links
Mass flux links connect pathway elements within a pathway network.
Behavior of a pathway network is primarily controlled by the manner in which mass flux links are defined.
Five types:
    Advective
    Diffusive
    Three special purpose types (will not discuss)
Multiple links can be made between/among pathways.
Mass fluxes are vectors by species with dimensions of mass/time.

## Slide 32: Example2: Simple Advection
Assume 10 g/day of A and B are added to Tank1 for 5 days (neither species decays)
Tank2 initially has no species mass
Both tanks contain constant volume of 10 m3 of Water and 10kg of solids; the tanks are well-mixed
Solid has a dry density of 2000 kg/m3, and a porosity of 0.3
Partition coefficients in Solid:
  A: 1 m3/kg
  B: 0 m3/kg
Water flows from Tank1 to Tank2 and then out of system (to a “sink” Cell) at 5 m3/day
Tank1
Tank2
“Clean” water
10 g/day added for 5 days
Cell3 (Sink)

## Slide 33: Equations Solved by GoldSim

## Slide 34: Example3: Advection With Solubility
Start with last example
Delete species A
Assume species B has solubility of 1 mg/l
Note: this is a very simple way to represent solubility constraints, and a much more detailed approach accounting for the actual geochemical behavior is often necessary (e.g., linking dynamically or through lookup tables to a geochemical equilibrium code)

## Slide 35: Diffusive Mass Flux Links
Implements molecular diffusion among pathways.
Transport in a stagnant or slowly moving fluid via molecular diffusion
Diffusive flux is bi-directional (unlike advective links, mass can move in either direction). Mass will move from high concentration to low concentration, driven by the concentration gradient between the cells.

## Slide 36: Example4: Diffusion
Cover on contaminated sediment is 0.5 m thick
Area of material is 10,000 m2
Well-mixed Pond is on top of sediment (1 m deep)
Cover is made of a sand with a dry density of 1600 kg/m3, a porosity of 0.3, tortuosity of 1.0, and 0.0 partition coefficient
Diffusivity = 1E-9 m2/sec
Contaminated sediment is at a constant concentration of 10 mg/l
Discretize into 5 cells and simulate for 100 yr (0.1 yr timestep)

## Slide 37: Cells Can Represent Any Geometry

## Slide 38: How to Model Dispersion?
Aquifer Pathways

## Slide 39: Aquifer Pathway Element
Internally, GoldSim uses a series of Cells to create the Aquifer Pathway.
The Aquifer Pathway incorporates:
one-dimensional advection
longitudinal dispersion
Retardation (due to porous infill)
Decay and ingrowth
Transport on suspended particulates

## Slide 40: Example5: Cylinder - Aquifer Pathway
5 m cylinder filled with Water and Sand
Sand has porosity 0.3, dry density 1600 kg/m3
Column cross-sectional area 1 m2
Water flows through column at 1 m3/yr
Dispersivity = 10% of length
Cl and Organic added at 10 g/yr
Kd for organic to Sand = 1.875E-4 m3/kg

## Slide 41: Combining Cells and Aquifers

## Slide 42: Coupling Flow and Transport Models
If the Flow is steady, no reason to model the flow system
If flow is transient, must couple these
  Use Reservoirs or Pools and Material Delays to model flow system
  Outputs of these elements are input to CT elements

## Slide 43: Example6: Combining Flow and Transport
Pond1 (a lined pond):
  Initial volume: 1000 m3
  Initial concentration= 0mg/l
  Discharge rate into Pond1: 4 m3/day
  Capacity: 1500 m3
  Concentration of Zn in discharge: 0.03 mg/l
  Pond1 overflows to Pond2
Pond2:
  Initial Volume = 500 m3
  Initial concentration = 0mg/l
  Seeps to a groundwater pathway based on volume (1%/day * volume)
Groundwater pathway:
  Total flow: 10 m3/day
  Area = 100 m2
  Length = 100 m; Dispersivity = 10% of path length
  Filled with Sand with porosity of 0.2 and density of 2000 kg/m3
Discharges to a small stream with flow rate of 1000 m3/day
  Stream reach into which discharge occurs has volume of 10 m3

## Slide 44: This is only the tip of the iceberg…
Many advanced features not discussed here:
  Transport on suspended particulates
  Water treatment (e.g., remove a certain fraction of incoming mass from a Cell)
  Other transport mechanisms (neither advective or diffusive): plant transport
  Matrix diffusion in fractures
  Linking to external transport models
  Simulation of complex source terms (the Source element)
  Calculation of impacts to receptors (the Receptor element)
  Auto-generation of large Cell nets (Cell Net Generator element)

## Slide 45: Summary
The Contaminant Transport Module is a complex and powerful add-on module for GoldSim
You can create extremely complex multi-dimensional models using only Cells and Aquifers
Not intended to build highly discretized models
  In many cases, it can be argued that this is not necessary or appropriate
Best way to learn:
  Online Course
  User Manual
  Example models in Model Library
  Send questions to GoldSim