## Slide 1: Introduction to GoldSim Course
September 9, 2024
Instructor: Jason Lillywhite

## Slide 2: Workshop Agenda
Morning
  Introduction to GoldSim
  The GoldSim User Interface
  Basic Concepts and Features
  Building Simple Models
Afternoon
  Feedback, Events and Delays
  Probabilistic Modeling
  Advanced Concepts and Features
  Introduction to the Contaminant Transport Module
Wifi:
MarriottBonvoy_Conference
Password: goldsim24

## Slide 3: Workshop Objectives
Become familiar with the GoldSim framework
Know how to build simple models
Learn how to get answers when you have questions
Not to learn every single feature in GoldSim
Notes: Learn the fundamentals of how GoldSim carries out its calculations
  You should not use “black boxes”; if you don’t understand how a tool works, don’t use it.

## Slide 4: What is GoldSim?
A dynamic simulation tool for
  Testing theories
  Understanding system behavior
  Making informed decisions about the management and development of resources
Unique qualities:
  Highly graphical user interface
  Probabilistic simulator
  Continuous and discrete
Notes: - Requires no programming expertise
- Similar to a spreadsheet, but:
  Graphical so models are easier to maintain and explain to others
  Understands concept of “time”
  GoldSim models are much more realistic than anything that can be created using a spreadsheet

## Slide 5: Applications
Chart: 
| Water Resources and Mining | Energy | Radwaste | Engineering Design and Risk | Other
Sales | 0.55 | 0.05 | 0.19 | 0.06 | 0.15

## Slide 6: Examples

## Slide 7: Mine Water Balance

## Slide 8: Mine Water Balance

## Slide 9: Tailings Facility

## Slide 10: Generic LLRW PA Model

## Slide 11: Water Supply Reliability Model

## Slide 12: Water Rights Analysis
Notes: The purpose of this model was to provide a model that would help a large and diverse stakeholder group come to a consensus on a preferred water supply alternative for a growing water demand. The model includes logic that allocates water to more than 30 diverters using a complex priority system based on state issued water rights. An integrated approach was used in this model in order to conceptualize aspects from multiple disciplines, including hydrologic, regulatory, and economic considerations. Model scenarios included an evaluation of many reservoirs, pumps, pipes, canals, and environmental constraints. An interactive user interface was created to modify scenarios during critical stakeholder meetings, which helped streamline the decision making process.

## Slide 13: Water Supply Operations Model
Notes: This model uses highly visual representations of a water system to provide an interface that was used by water system operators to simulate and test start up scenarios for a newly constructed water system. The system consists of two water treatment plants, reservoirs, a large pump station, sleeve valve vault, and bi-directional, 20 mile pipeline. The model is run in slow motion, mimicking real-time operations of the system so that operators could play what-if scenarios by interacting with the model as if they were actually operating the real system.

## Slide 14: Hydraulics and Hydrology

## Slide 15: Oil Sands Process Model

## Slide 16: Alumina Refinery Model

## Slide 17: City of Melbourne’s Forecast Population

## Slide 18: Strategic Planning for Whisky Stocks

## Slide 19: Introduction to GoldSim

## Slide 20: How do you build a GoldSim model?
Graphical objects (elements)
Influence lines
Schematic diagram of model logic

## Slide 22: Basic Concepts
Go to the Exercises Presentation…

## Slide 23: Go to GS_Basic_Exercises.pptx

## Slide 24: Advanced Topics

## Slide 25: Modeling Scenarios
6340
6350
6360
6370
6380
6390
6400
2020
2030
2040
2050
2060
2070
2080
2090
Elevation (ft)
Time
Water Level in Reservoir
Elevation (#1)
Low Diversion
Mid Diversion
High Diversion
0.0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1.0
1000
2000
3000
4000
5000
Probability of Not Exceeding
(kAF)
Reservoir Volume at End of Simulation
(Low Diversion)
(Mid Diversion)
(High Diversion)

## Slide 26: Modeling Scenarios
Specify different input data for each scenario
Run the model for each scenario
Save the results for each scenario
Compare results

## Slide 27: The Scenario Manager (F7)
Scenario Name
Description
Execute Scenario Run
Run All
Active Scenario
Scenario Data

## Slide 28: Scenario Data Table

## Slide 29: Scenario Data Element
Data Element
Check on/off
Summary of scenario data

## Slide 30: Dashboard Authoring Module
Interface for models
Create a "control panel“
  Buttons
  Sliders
  Display panels
  Instructions, etc.
Custom simulation applications for distribution to end users
For lay audience
Used for interaction with the Player
Notes: Allows you to design and construct a "dashboard" interface for models.
  The interfaces can be designed to look like "control panels", with buttons, gauges, sliders and display panels, instructions, etc.
Enables you to use GoldSim as a high-level programming language to create custom simulation applications for distribution to end users who may not necessarily be modelers.
A “dashboarded” model can be viewed and run using the free GoldSim Player.

## Slide 31: Dashboard Controls
Input controls:
Output controls:
Buttons:

## Slide 32: Examples…
© GoldSim Technology Group LLC, 2018

## Slide 33: Script Element
Write custom scripts
Define and assign variables
Logical control
  If/Else
  For/Do/While loops
  Break & Continue
Comments
Log Messages
Interrupt with Errors/Warnings

## Slide 34: Linking to Excel
Already have seen:
  Importing from Excel to Lookup Table elements
  Importing from Excel to Time Series elements
  Exporting to Time History Result elements
Spreadsheet element can:
  Import from Excel
  Exporting to Excel

## Slide 35: Linking to External Programs
You can dynamically link an external program to GoldSim.
It behaves identically to an Expression element, but instead of using an equation, GoldSim dynamically calls and runs the external program.
This allows complex external programs to be linked directly into the probabilistic, graphical GoldSim framework.

## Slide 36: Advanced Timestepping Options
Periods with shorter timesteps
Dynamic control of timesteps
Containers with their own timesteps

## Slide 37: Optimizing Your Model
Objective function
Goal
Constraints (optional)
Optimization variables
Automatically run multiple times
Finds a solution with optimized objective function
Notes: Optimization Inputs:
  an objective function (a specific result that you would like to minimize or maximize),
  an optional constraint (a condition that must be met), and
  one or more optimization variables (variables in your model that you have control over).
GoldSim then runs the model multiple times, systematically selecting combinations of values for each of the optimization variables.
Applications:
  Optimizing a design or plan
  Calibrating to historic data

## Slide 38: Sensitivity Analysis
Computes statistical measures
  Based on multiple Monte Carlo simulations (all variables changed simultaneously)
Graphical sensitivity analyses (tornado charts, x-y charts)
  Variables of interest are changed while holding all other variables constant

## Slide 39: Presentation and Documentation
Presentation Tools:
  Dashboards
  Elements themselves
  Inserted graphics
  Text boxes
  Notes
  Hyperlinks
Player model can be used as “Documentation”
Notes: One of the most powerful and unique features of GoldSim is its ability to incorporate graphics, text, images and hyperlinks into a model.
These capabilities, coupled with GoldSim’s ability to create “top-down” models, allow you to describe your model at different levels of detail to different audiences

## Slide 40: Images, Graphics and Text

## Slide 41: Notes and Hyperlinks

## Slide 42: Examples of Documentation

## Slide 43: Versioning

## Slide 44: Introduction to the Contaminant Transport Module

## Slide 45: GoldSim and the Contaminant Transport Module
  The basic GoldSim framework consists of a flexible set of tools for creating dynamic, probabilistic simulations of nearly any kind of complex system.
    These tools are very abstract (like a programming language).
    They simply carry out mathematical calculations (e.g., numerical integration) that are applicable to many types of problems.
  In order to simulate some kinds of complex systems, such tools are not sufficient. Therefore, GoldSim has several specialized extension modules to facilitate simulation of some types of systems.
  The Contaminant Transport Module is a set of specialized elements that are added to GoldSim to support complex contaminant transport simulations.

## Slide 46: GoldSim and the Contaminant Transport Module
  The Contaminant Transport Module is powerful and complex.
  Today we will simply provide an overview.
  Due to the limited amount of time, will not work through examples together. Instead, I will simply present a number of examples.
  The Contaminant Transport Module is described in great detail in a free online course:

## Slide 47: GoldSim and the Contaminant Transport Module
  The module is used to simulate the movement of mass (typically contaminants) through natural (and engineered) systems.
  Produces predictions of mass transport rates at defined locations, concentrations in specified environmental media (e.g., water, soil), and impacts to defined human receptors (e.g., dose, health risk).
  Processes that can be simulated include mixing, solubility constraints, sorption, advection, dispersion, diffusion, and chemical reactions and radioactive decay and ingrowth.
  Can this be done with basic GoldSim?
    Simple mixing problems could be simulated, but any complex processes would be difficult or impossible to simulate without the Contaminant Transport Module.

## Slide 48: There are Two Contaminant Transport Module Versions
  CT and RT
  RT includes several specialized features primarily used to simulate the transport of radionuclides (e.g., simulation of decay chains)

## Slide 49: How Detailed and Highly Discretized Should Your Contaminant Transport Model Be?
Just because you can build a large, highly discretized model does not mean you should.
  How much uncertainty do you have in the source?
  How much uncertainty do you have in the key transport properties (e.g., partition coefficients, solubilities)?
  Do you really understand the dispersive characteristics of the system?
As a general rule, our ability to predict concentrations is much poorer (i.e., subject to greater uncertainty) than our ability to predict flows.

## Slide 50: Since all models are wrong the scientist cannot obtain a "correct" one by excessive elaboration… Just as the ability to devise simple but evocative models is the signature of the great scientist, so overelaboration and overparameterization is often the mark of mediocrity. George Box, Science and Statistics (1976)

## Slide 51: Top-Down Modeling

## Slide 52: Uranium Mine Closure

## Slide 53: Mine Water Treatment

## Slide 54: Shallow Radioactive Waste Disposal Facility

## Slide 55: Deep Radioactive Waste Disposal Facility

## Slide 56: Proposed Yucca Mountain Repository

## Slide 57: Contaminant Transport Module
Adds specialized elements to facilitate simulation of contaminant transport through engineered and natural environmental systems
r
RT Module Only

## Slide 58: Contaminant Transport Module
Provides a basic framework for modeling fate and transport of dissolved, sorbed and/or suspended contaminants through engineered and natural systems.
Complexity of the model is determined by the user.
While incorporating some basic physics (e.g., conservation of mass, decay and ingrowth, diffusion, partitioning), very few assumptions built into code in order to maximize flexibility.
Heavily utilizes arrays.

## Slide 59: Steps for Modeling Contaminant Transport
Specify species to be modeled.
Specify the transport and storage media within the system to be modeled (e.g., water, air, sediment, soil).
Specify the transport pathways through which mass is transported and stored.
Define the source terms (initial and/or boundary conditions).
Define the impacts of the species (e.g., dose) on defined receptors.

## Slide 60: Defining Species
Species element

## Slide 61: Environmental Media
Basic “building blocks” of transport pathways
  mass transport calculations are based largely on media properties
  Two types: Fluids and Solids

## Slide 62: Transport Pathways
Transport pathways represent those parts of the system through which species mass is transported and/or in which species mass is stored.
  Tanks, ponds, aquifers, lakes, soil columns, etc.
You define the properties of the pathways, such as geometry, volume, and pathway discretization.
You define which media (e.g., air, water, sediments, rock) types are present in the pathway.

## Slide 63: Transport Pathways
Pathways can be thought of as transfer functions.
Each pathway type (or transfer function) assumes or represents a particular range of physical transport processes.

## Slide 64: Transport Pathways
We will focus on Cells and Aquifers today.
GoldSim provides five type of pathways:

## Slide 65: Transport Pathways
You create a mass transport system by defining a network of transport pathways using mass flux links among the pathways.

## Slide 66: Pathways Mass Balance
Species mass is conserved.
The Contaminant Transport Module simulates mass transport so it solves for the mass of each species in each transport pathway.
  The water, or other media, balance is not a part of the transport module solution.
  Media advection rates are inputs (and not solution values) for transport pathways.
    You can link the transport media advection rates to a water balance model (or other media balance model) in order to enforce both a water balance and species mass balance.

## Slide 67: Contaminant Sources
You can specify initial and boundary conditions in Pathways.
In some cases, however, direct specification of an initial condition or rate of input is not possible. The RT Module allows you to simulate a source term using a Source element.
The Source element simulates:
  Failure of barriers containing the mass
  Degradation of matrix material (e.g., grout) in which the mass is bound
  Particularly useful when simulating engineered barrier systems
Won’t discuss further today.

## Slide 68: Receptors
The objective of many studies is not only to compute contaminant concentrations and fluxes at various locations, but to also compute the impact of these contaminants on specified receptors.
GoldSim provides a Receptor element that facilitates the conversion of contaminant concentrations in media within pathways to impact to defined receptors (e.g., dose, health risk).
Won’t discuss further today.

## Slide 69: Example1: Partitioning and Decay in a Cell
Assume 10 g of species C and D exists in Cell
The cell contains 10 m3 of Water and 10 kg of Sand
Sand has a dry density of 1600 kg/m3, and a porosity of 0.3
Partition coefficient for C in Sand: 2 m3/kg
Partition coefficient for D in Sand: 0 m3/kg
C decays with a half-life of 5 years
Run for 20 years

## Slide 70: Cell Pathways
Act as mixing cells
Can specify multiple media
Mass is instantly mixed and equilibrated (partitioned) within cell
Solubility constraints can be imposed in cell
Can have specified initial/boundary condition
Behavior of cell network is mathematically equivalent to network of finite difference nodes

## Slide 71: Equations Solved By GoldSim

## Slide 72: Example1a: Partitioning Decay and Ingrowth in a Cell
Assume C decays to D

## Slide 73: Equations Solved by GoldSim

## Slide 74: Mass Flux Links
Mass flux links connect pathway elements within a pathway network.
Behavior of a pathway network is primarily controlled by the manner in which mass flux links are defined.
Five types:
    Advective
    Diffusive
    Three special purpose types (will not discuss)
Multiple links can be made between/among pathways.
Mass fluxes are vectors by species with dimensions of mass/time.

## Slide 75: Example2: Simple Advection
Assume 10 g/day of A and B are added to Tank1 for 5 days (neither species decays)
Tank2 initially has no species mass
Both tanks contain constant volume of 10 m3 of Water and 10kg of solids; the tanks are well-mixed
Solid has a dry density of 2000 kg/m3, and a porosity of 0.3
Partition coefficients in Solid:
  A: 1 m3/kg
  B: 0 m3/kg
Water flows from Tank1 to Tank2 and then out of system (to a “sink” Cell) at 5 m3/day
Tank1
Tank2
“Clean” water
10 g/day added for 5 days
Cell3 (Sink)

## Slide 76: Equations Solved by GoldSim

## Slide 77: Example3: Advection With Solubility
Start with last example
Delete species A
Assume species B has solubility of 1 mg/l
Note: this is a very simple way to represent solubility constraints, and a much more detailed approach accounting for the actual geochemical behavior is often necessary (e.g., linking dynamically or through lookup tables to a geochemical equilibrium code)

## Slide 78: Diffusive Mass Flux Links
Implements molecular diffusion among pathways.
Transport in a stagnant or slowly moving fluid via molecular diffusion
Diffusive flux is bi-directional (unlike advective links, mass can move in either direction). Mass will move from high concentration to low concentration, driven by the concentration gradient between the cells.

## Slide 79: Example4: Diffusion
Cover on contaminated sediment is 0.5 m thick
Area of material is 10,000 m2
Well-mixed Pond is on top of sediment (1 m deep)
Cover is made of a sand with a dry density of 1600 kg/m3, a porosity of 0.3, tortuosity of 1.0, and 0.0 partition coefficient
Diffusivity = 1E-9 m2/sec
Contaminated sediment is at a constant concentration of 10 mg/l
Discretize into 5 cells and simulate for 100 yr (0.1 yr timestep)

## Slide 80: Cells Can Represent Any Geometry

## Slide 81: How to Model Dispersion?
Aquifer Pathways

## Slide 82: Aquifer Pathway Element
Internally, GoldSim uses a series of Cells to create the Aquifer Pathway.
The Aquifer Pathway incorporates:
one-dimensional advection
longitudinal dispersion
Retardation (due to porous infill)
Decay and ingrowth
Transport on suspended particulates

## Slide 83: Example5: Cylinder - Aquifer Pathway
5 m cylinder filled with Water and Sand
Sand has porosity 0.3, dry density 1600 kg/m3
Column cross-sectional area 1 m2
Water flows through column at 1 m3/yr
Dispersivity = 10% of length
Cl and Organic added at 10 g/yr
Kd for organic to Sand = 1.875E-4 m3/kg

## Slide 84: Combining Cells and Aquifers

## Slide 85: Coupling Flow and Transport Models
If the Flow is steady, no reason to model the flow system
If flow is transient, must couple these
  Use Reservoirs or Pools and Material Delays to model flow system
  Outputs of these elements are input to CT elements

## Slide 86: Example6: Combining Flow and Transport
Pond1 (a lined pond):
  Initial volume: 1000 m3
  Initial concentration= 0mg/l
  Discharge rate into Pond1: 4 m3/day
  Capacity: 1500 m3
  Concentration of Zn in discharge: 0.03 mg/l
  Pond1 overflows to Pond2
Pond2:
  Initial Volume = 500 m3
  Initial concentration = 0mg/l
  Seeps to a groundwater pathway based on volume (1%/day * volume)
Groundwater pathway:
  Total flow: 10 m3/day
  Area = 100 m2
  Length = 100 m; Dispersivity = 10% of path length
  Filled with Sand with porosity of 0.2 and density of 2000 kg/m3
Discharges to a small stream with flow rate of 1000 m3/day
  Stream reach into which discharge occurs has volume of 10 m3

## Slide 87: This is only the tip of the iceberg…
Many advanced features not discussed here:
  Transport on suspended particulates
  Water treatment (e.g., remove a certain fraction of incoming mass from a Cell)
  Other transport mechanisms (neither advective or diffusive): plant transport
  Matrix diffusion in fractures
  Linking to external transport models
  Simulation of complex source terms (the Source element)
  Calculation of impacts to receptors (the Receptor element)
  Auto-generation of large Cell nets (Cell Net Generator element)

## Slide 88: Summary
The Contaminant Transport Module is a complex and powerful add-on module for GoldSim
You can create extremely complex multi-dimensional models using only Cells and Aquifers
Not intended to build highly discretized models
  In many cases, it can be argued that this is not necessary or appropriate
Best way to learn:
  Online Course
  User Manual
  Example models in Model Library
  Send questions to GoldSim

## Slide 89: Elliot Bay Dinner Cruise
Dinner cruise along the Seattle waterfront a private yacht
Bring your name tag
Boat loads Bell Harbor Marina, Pier 66 – 2203 Alaskan Way, Seattle (directly across from the Marriott hotel)
Access: walk around Anthony’s restaurant and through the gatehouse
Timeline:
  5:20 PM: Meet in lobby
  5:30 PM: Boarding
  6:00 PM: Sailing
  9:00 PM: Return and depart the boat