## Slide 1: Modeling Runoff
GoldSim User Conference 2024

## Slide 2: Introduction
Weather and climate play a significant role in systems being modeled in GoldSim
Growing need for native models to reflect uncertainty
GoldSim solution
  Propagate uncertain inputs to the outputs
  Lumped, conceptual models are a good fit
  Linkage to other tools

## Slide 3: Considerations for Runoff Modeling in GoldSim
What specific questions or problems are you aiming to address?
What are the primary goals of the modeling effort?
Level of Detail Required
End User Requirements
Calibration accuracy
What testing and validation steps are necessary to ensure model reliability?
How will the model integrate with other tools and data sources within GoldSim?
Notes: Level of Detail Required
- How detailed does the model need to be to provide accurate and useful answers?
- What level of complexity is necessary to achieve your objectives?
End User Requirements
- Who will be using the model, and what are their needs?
- How will the end users interact with the model and interpret its results?
Key Performance Indicators (KPIs)
Calibration accuracy
Resource management metrics
User experience and satisfaction
Exploratory Analysis
What preliminary analyses are needed to inform the model structure and parameters?
Report Findings
How will the results be reported and communicated to stakeholders?
Testing Protocols
What testing and validation steps are necessary to ensure model reliability?
GoldSim Integration
How will the model integrate with other tools and data sources within GoldSim?

## Slide 4: Lumped Conceptual Model
Conceptual representation of the rainfall-runoff process
Aggregate catchment variability into a single set of parameters
Ideal for daily or larger time steps
Integrates into larger models
A good fit for GoldSim
Contrast to “process-based” or “physical based” models (SWAT, VIC)
Model
Data3
Data2
Data1
TimeSeries3
TimeSeries2
TimeSeries1

## Slide 5: Components of a Conceptual Model
Main components:
  Precip and PET
  Interception
  Baseflow and Surface recession flows
Use of “buckets” in parallel and in series with recession outflows
Examples: AWBM, HSPF, GR4J

## Slide 6: Potential Evapotranspiration
Monthly values in Lookup table
Methods:
  Hamon (Tavg, Lat)
  Hargreaves-Samani (Tmin, Tmax, Lat)
  FAO Penman Monteith (Tmin, Tmax, Lat, Sunshine, Wind)

## Slide 7: Snow Accumulation and Melt
CemaNeige
  Paired with GR4J runoff model
  4 calib. parameters
Snow-17
  NWS River Forecast System
  10 calibration parameters
Output: Rain and melt water
SNOTEL site at Paradise, Mount Rainier. Source: Natural Resources Conservation Service

## Slide 8: Examples in the GoldSim Library
Climate:
  Sample historical time series
  Stochastic weather generators
Runoff:
  Evaporation and ET Models
  Water demand estimators
  Snow
  Simple runoff estimators
  Conceptual Models: AWBM, GR4J, SAC-SMA, HSPF, and more
River routing:
  Usually not applicable for time steps < 1 day
  Simple delay and dispersion
  Muskingum-Cunge routing model

## Slide 9: AWBM
Most widely used in GoldSim models
4 calibration parameters
  Soil depths (vector)
  BFI
  2 Recession constants
Baseflow Store
Surface Runoff
Routing Store
Baseflow Runoff
Surface Runoff
Routed
Surface
Runoff
Total Runoff
Rainfall Excess
Surface Stores
Pot. ET
Rainfall
Baseflow
Recharge
C1
C2
C3
A1
A2
A3

## Slide 10: GR4J
4 calibration parameters
  Production capacity
  Lag
  Routing capacity
  Exchange coefficient

## Slide 11: SAC-SMA

## Slide 12: HSPF (Pervious Catchment)

## Slide 13: Interaction with Other Components
Choose the components you plan to assemble for the runoff model before you dive into model construction.
The components you choose will partly be driven by how much detail you plan to include.

## Slide 14: Building a Runoff Model in GoldSim

## Slide 15: Delineate the Catchments
Map drawing tools with the terrain layer turned on.
Draw polygons along contour lines to delineate the elevation zones used for the snow melt model and/or runoff routing model.
GIS tools could also be used for this same purpose.

## Slide 16: Snow vs. Runoff Delineation
Watershed broken into catchments
  Soil, vegetative cover, land use
Snowmelt models require elevation-based zones
  Temperature differences
Catchments
Snow Zones

## Slide 17: Conceptualizing the Catchment
Each runoff model represents a catchment within a watershed
Lump parameters for area
Single discharge point
Link to other catchments… How?

## Slide 18: Method 1: Localized Containers
Copy and paste containers
Simple to build but more difficult to maintain and change down the road.
Once you have them pasted, link the flows from each to build the flow network within the watershed.
Sum for flow junctions
Allocator for diversions

## Slide 19: Method 2: Clones
Requires some careful setup
Easier to change and reconfigure down the road.
Each catchment contains a generic “Runoff” clone
Now any future changes you make to the "Runoff" module will be replicated to the clones.

## Slide 20: Method 3: Arrays
Not as visual
No schematic diagram showing where water is flowing
Input data much easier to deal with

## Slide 21: Routing Flows
Sum elements for junctions
Muskingum Cunge for reaches with adequate residence time

## Slide 22: Routing with Losses and Diversions
Network of watersheds connected at junctions
Seepage losses function of flow
Delay and …attenuation?
  Muskingum Cunge
  Exponential decay function using series of stores
River diversions
Storage outflows feedback loop
Human controlled components added to model
  River diversions
  Agricultural, industrial, municipal water use

## Slide 23: Integrated Model

## Slide 24: Extending GoldSim
Script elements
Excel with macros
Compiled Win32 DLL
  EPA SWMM

## Slide 25: Questions?