## Slide 1: Simulating Precipitation
GoldSim User Conference 2024
Notes: Welcome to our session on simulating precipitation with GoldSim.

## Slide 2: Introduction
Weather impacts most GoldSim models
Including weather in your model involves:
  Relying on measured data
  Incorporating uncertainty
GoldSim can help with both of these requirements
Rick: 425-894-5172. Mark: 206-561-4300
Meet in lobby at 5:15pm
No bags allowed in stadium

## Slide 3: Time Series Element
GoldSim’s Time Series element is a powerful tool for incorporating precipitation data.
It allows for:
  Time shifting
  Lookup

## Slide 4: Visual Inspection: A Critical Step
Visual inspection is essential for validating historical data:
  Zoom out: Align simulation start and end dates with historical records. Scan for gaps and outliers.
  Zoom in: Use time shifting and run shorter periods with multiple realizations. Zoom in to scrutinize details.
Calculate statistics and compare them to ensure data integrity.

## Slide 5: Period Summaries: Annual Insights
View cumulative results
Gain insights into long-term trends
This helps in understanding yearly variations in precipitation.

## Slide 6: Period Statistics: Annual and Monthly
Each realization represents a historical year
Time Series shifting option (annually)
Monthly and Annual total statistics
Consider wrapping behavior

## Slide 7: Historical Time Series
Visualizing daily time series data
Annual distributions
Monthly and annual summaries
Period Statistics

## Slide 8: Daily Precipitation Simulation
Sampling of historical time series (Time Shifting)
  Random year vs. sequential
Stochastic weather generators
  First order Markov Chain Process
Others not implemented in GoldSim:
  Multiple Point Statistics (MPS)
  Generalized Linear Models (GLMs)
  Neural Networks and Machine Learning
Notes: Multiple Point Statistics (MPS): This method uses training data to reproduce complex statistical structures and patterns found in the data. It aims to capture the spatial and temporal variability of precipitation1.
Generalized Linear Models (GLMs): GLMs can model the occurrence and amount of precipitation separately, using predictors such as temperature, humidity, and atmospheric pressure. This approach allows for the inclusion of covariates and can handle non-linear relationships.
Neural Networks and Machine Learning: These techniques use large datasets to train models that can predict precipitation based on various input features. They can capture non-linear relationships and interactions between variables.

## Slide 9: Modeling with Markov Chains
A mathematical model to describe a sequence of events
Probability of next event depends only on current state of system
Useful in a wide variety of fields including finance, physics, and engineering
Help predict future events and make decisions based on probabilities
Notes: A 1st order Markov chain process is a mathematical model that is used to study the evolution of a sequence of random variables. In this model, the probability of the next event depends only on the current state of the system, not on any events that occurred before. Markov chain models are useful in a wide variety of fields including finance, physics, and engineering. They can be used to predict future events and make decisions based on probabilities. A probability distribution or a state transition diagram can be used to visualize the model.

## Slide 10: Markov Chain-gamma Model
Use probabilities to determine wet or dry state
Probability changes based on yesterday’s state (Markov Chain)
On wet days, sample random daily rate from gamma distribution

## Slide 11: Order of Markov Chains
Second order Markov can take into account the last 2 days instead of just the last day
More accurate prediction model for some areas but a lot more work
1st Order
2nd Order

## Slide 12: Weather Generation Model “WGEN”
Stochastic weather generator
Authors: C. W. Richardson and D. A. Wright Agriculture Research Service (USDA), August 1984
Parameter Generator “WGEN PAR” generates parameters using historical data

## Slide 13: WGEN Modeling Process
Four parameters constant for each month
First order Markov chain with gamma distribution
Results in probabilistic daily precipitation
Intended for a Monte Carlo simulation

## Slide 14: WGEN Outputs
Simulates long-term weather data
  Daily precipitation (Markov chain)
  Min/Max daily temperature and solar radiation (weakly stationary generating process)
Plug and play within GoldSim framework

## Slide 15: Limitations
Missing driest and wettest years on record.

## Slide 16: PrecipGen
Focus on Precipitation
Captures behavior during dry and wet years
Expanded inputs
Mean and Standard Deviation of inputs

## Slide 17: PrecipGen Modeling Process
Four parameters constant for each month
PrecipGen uses first order Markov chain with gamma distribution
Results in probabilistic daily precipitation
Intended for a Monte Carlo simulation

## Slide 18: New PrecipGen Components
Long-term variability using stochastic elements, resampling annually
Annual autocorrelation
Statistical correlation between parameters (PWW-PWD, PWW-Mean)

## Slide 19: PrecipGen Results

## Slide 20: Incorporating Climate Change
Main parameters become probability distributions
Correlations
Autocorrelation of annual totals

## Slide 21: PrecipGen Demo