## Slide 1: Modeling Ponds and Reservoirs
GoldSim User Conference 2024
Instructor: Jason Lillywhite

## Slide 2: Introduction
Basic elements
Conceptual models
Simulating outflows
Advanced modeling techniques
Notes: This slide will provide an introduction to the GoldSim Model, its purpose, and the objectives of the session. A brief agenda will also be presented.

## Slide 3: Basic Elements in a GoldSim Model
Physical constraints
  Geometry
  Uncontrolled flows
  Hydraulic structures
Operational Rules
  Imposing custom “bound” or “target”
  Triggering and time steps
Notes: This slide will explain the basic functionality of the GoldSim Model, including how inflows accumulate, the concept of outflows restricted to inflow when volume is at lower bound, and the difference between imposing soft vs hard bounds. Examples will be given to help explain these concepts.

## Slide 4: Elements to Build a Pond Model
Volume-Depth-Area relationship
  Lookup tables
Uncontrolled flows
  Precip/evaporation
  Inflows
  Sediment load
Hydraulic structures
  Weir/orifice flow, energy equation, etc.
  Conceptualize when Q*dt > V
Operational rules
  Many types

## Slide 5: Geometry
Volume to Elevation
Volume to Area
Elevation : Area (use TBL_Integral)
Linear interpolation
Changing over time?
  2 dimensional lookup

## Slide 6: Precipitation and Evaporation
Precipitation on the watershed around the lake
Evaporation from water surface
Negative feedback loop

## Slide 7: Sediment Load
As solids volume accumulates, water capacity decreases
As capacity decreases, this can push water out

## Slide 8: Hydraulic Structures
Spillway
Orifice
Pump
Gate

## Slide 9: Physically Based Outflow Simulation
Rapid Feedback Loops:
  Physical responses in hydraulic systems (e.g., gates, weirs) adjust rapidly throughout the day.
  These responses create feedback loops that continuously change based on real-time conditions.
Modeling Challenges:
  GoldSim models typically use larger time steps
  Rapid changes within a day are not captured in this time frame.
Need for Conceptualization:
  To accurately represent these rapid changes, we need to
    Shorten the time step or…
    Conceptualize the physical responses
Notes: This slide will explain the different types of hydraulic controls in GoldSim Model, including gates, weirs, orifice, and pumps. The factors affecting hydraulic control, such as water pressure, flow rate, and structural dimensions, will also be discussed.

## Slide 10: Strategies for Conceptualizing Flows
On/Off using “Dead Band”
Proportional
Volume-Discharge rating curve
Others: PID controller
Mixed hydraulic and conceptual when near bounds
  min(weir_flow, Volume / 1 day)
Notes: This slide will explain operational control in GoldSim Model, including how to model it conceptually, the different components of operational logic, and how to use events and lookup tables. The slide will also discuss the combination of hydraulic and operational control.

## Slide 11: Oscillations at Bounds
Understanding how Bounds work
Inserted time steps
Strategies to avoid oscillations

## Slide 12: Hydraulic + Operational (Shutoff)
V >> shutoff Volume: Orifice flow is controlling
When V ~= shutoff volume, Orifice flow is not controlling

## Slide 13: Hydraulic + Operational (Proportional)
V >> shutoff Volume: Orifice flow is controlling
When V ~= shutoff volume, Orifice flow is not controlling

## Slide 14: Reservoir with Multiple Operating Levels
Managing Multiple Levels
Demo strategies
Notes: This slide will explain how to manage multiple levels in a reservoir in GoldSim Model. Strategies and examples will be discussed, and the benefits and challenges of using a multi-level reservoir will be highlighted.

## Slide 15: Case Study / Example
Real-World Application
Detailed example of a pond or reservoir model
Lessons learned
Notes: This slide will provide a case study example of a real-world application of GoldSim Model in a pond or reservoir model. A detailed example will be given, and lessons learned from the example will be discussed.

## Slide 16: Looping Containers
Iteratively solve for request using feedback from another component
Easy to build
Somewhat limiting
  Another tool required for a min cost, max flow type of linear programming solver

## Slide 17: Questions?
Notes: This slide will provide a conclusion to the GoldSim Model presentation. A summary of key points will be presented, and the main topics covered in the presentation will be recapped.