## Slide 1: Advanced Radionuclide Transport Modeling Concepts
Rick Kossik

## Slide 2: Outline
Specifying Model Species Using the ICRP Database
Simulating Engineered Barriers (the Source Element)
Modeling Isotopes
Correctly Representing Uncertainty in Key Parameters by Dealing with Correlations
Simulating Complex Diffusive Geometries

## Slide 3: Specifying Model Species Using the ICRP Database
GoldSim includes a built-in database of nuclide decay data (over 1200 nuclides) from the International Commission for Radiation Protections (ICRP) Publication 107.
Let’s walk through the steps for defining your species using this database.

## Slide 4: Specifying Model Species Using the ICRP Database
Open Species. Under Display, “Modeled Species” will be selected.
Select “All Species” from the Display field.
Filter by half-life (e.g., 1 hr).
Select the Include box for species that you know are in the inventory. You can click on the columns to help you find the species (e.g., U238).
Select “Modeled species + daughters” from the Display field.
Adjust Auto-include ICRP daughters to show appropriate range (e.g., > 1 yr).
Manually include important stable species (e.g., Pb) and important short-lived species (e.g., Rn222) that were not auto-included.
Delete the default user-defined species.

## Slide 5: Specifying Model Species Using the ICRP Database
What are the implications of “skipped” species in the decay chain?
U238 decay chain:
  U238 -> Th234 -> Pa234m -> U234 …
  Th234 and Pa234m are skipped due to short half lives
  U238 -> U234 …
It is important to account for these “skipped” radionuclides when computing doses.

## Slide 6: Simulating Engineered Barriers (the Source Element)
What does a Source element do?
  Accounts for failure of waste packages, degradation of waste matrix and transport out of waste packages to represent complex source terms.
When should you use a Source element?
  When you cannot accurately represent the source term using an equation (e.g., a boundary condition it a Cell).
This will often be the case if:
  the source term involves barriers that fail over time;
  the source term includes one or more matrix materials that release species mass as they degrade; and/or
  the source term is modified by reactions (e.g., decay and ingrowth) prior to and during release.

## Slide 7: Overview of Source Element
Represents a discrete number of packages.
The packages can have zero, one or two barriers.
  Barriers must fail before waste can be released.
Each package has one or more specified inventories.
  The inventory can be specified to be bound within a waste matrix.
  The inventory can exist inside first barrier, inside the second barrier, or bound inside the matrix.
Mass is exposed when barriers have failed and matrix has degraded.
Source elements are Containers. They contain one or more Inventory Cells (representing the interior of the packages) into which the exposed mass is placed.
Once mass it exposed it can then be transported out of the Inventory Cells via advective and diffusive processes.

## Slide 8: Waste Package Failure
Barrier failure is represented in terms of failure distributions.
This represents temporary variability in when a group of packages fail.
A failure distribution is a probability density function of failure at any given time.
GoldSim allows you to specify different types of failure distributions.

## Slide 9: Example: Loss of Containment
  We will model a single package (a drum).
  When the drum fails, the mass is exposed.
    Uniform failure distribution (10 years)
  Three species:
    X decays to Y (half-life of 5 years)
    Y and Z do not decay
    All three initially present at 100 g
Notes: Source1_Failure

## Slide 10: Degradation of Waste Matrix
If inventory is specified to be bound within a waste matrix:
  Species mass is exposed congruently with the degradation of the matrix. That is, mass is assumed to be uniformly distributed through the matrix, and the fraction of the mass that is released from the matrix is equal to the fraction of the matrix that has degraded.
  Matrix degradation does no start until after any barriers have failed.
  Matrix can degrade with a specified lifetime or at a specified rate.
  There is also a third option (Congruent Dissolution) in which the inventory is bound in a matrix, and the matrix degrades based on solubility-limited dissolution of one of the species.

## Slide 11: Example: Matrix Degradation
  We will model a single package (a drum).
    Uniform failure distribution (10 years)
  Three species:
    X decays to Y (half-life of 5 years)
    Y and Z do not decay
    All three initially present at 100 g
  Matrix lifetime = 3 years
Notes: Source2_Degradation

## Slide 12: Example: Multiple Packages
  10,000 packages
    Weibull failure distribution
  Two species:
    Neither decay; initially 100g present
    X not bound in matrix
    Y bound in matrix
  Matrix lifetime = 3 years
Notes: Source3_Multiple_Packages

## Slide 13: Complex Barrier Failure Distributions
The distribution does not have to start immediately.
You can multiple failure modes.
Some modes may only apply to a fraction of the packages.
Notes: Source4_Complex_Container_Failure

## Slide 14: Transporting Exposed Mass Out of Source
So far we have only exposed the mass, but have not transported it out of the Source.
Exposed mass is placed into one or more Inventory Cells.
You then can create advective and diffusive connections to transport the mass from the Inventory Cells to pathways outside of the Source.
Conceptually, the Inventory Cells represent the interior of the waste package.

## Slide 15: Example: Transporting Mass Out of Source
  Single package (representing a square underground vault)
  Fails uniformly (5 years)
  Vault is filled with Sand
  After failure, water flows horizontally through vault
  Three species:
    initially 100g present
    No decay
    Y has low solubility (X and Z infinitely soluble)
    Z partitions onto the Sand (X and Y do not)
Notes: Source5_Vault

## Slide 16: Transporting Exposed Mass Out of Source
Conceptually, the Inventory Cells represent the interior of the waste package.
But what if we have multiple packages? What do the Inventory Cells represent? How do we specify their inputs (dimensions, volume, etc.)?
Cells inside a Source are treated in a special way. GoldSim automatically scales the following properties:
  Volume and Mass of media in each Cell
  Flow Rate for advective connections
  Diffusive area for diffusive connections
These properties are scaled by the number of failed packages.
Hence, at any given time in a simulation, the Associated Cells actually represent the group of all the packages that have failed up to that time. In effect, GoldSim accounts for the presence of multiple packages by dynamically increasing the size of the Associated Cells.

## Slide 17: Example: Transporting Mass Out of Source with Multiple Packages
  100 packages (representing a square underground vaults)
  Fails according the Weibull distribution
  Vault is filled with grout
  Grout degrades over 2 years.
  After failure, water flows horizontally through vault
  Three species:
    initially 100g present
    No decay
    Y has low solubility (X and Z infinitely soluble)
    Z partitions onto the grout (X and Y do not)
Notes: Source6_Multiple_Vaults

## Slide 18: Source Summary
Accurately modeling all of the processes (waste package failure, matrix degradation, transport processes out of package) can result in a very complex source term that would be impossible to represent using a boundary condition equation.
We did not discuss inner barrier, which can complicate matter further.

## Slide 19: Modeling Isotopes
GoldSim allows you to enter some properties (e.g., solubilities, partition coefficients) as species properties or elemental properties.
  If you are modeling isotopes, these are elemental properties and should be entered as such.
  If entered as species properties, GoldSim will use the value for the first isotope of the element.
Ignoring stable species can lead to unrealistic results!
Notes: Source7a_Isotopes, Source7b_Isotopes

## Slide 20: Correctly Representing Uncertainty in Key Parameters
Many input parameters in a radionuclide transport model are highly uncertain (e.g., orders of magnitude)
  solubilities, partition coefficients
However, if we simply put these in as probability distributions we could actually create very unrealistic models.
Why? Because many parameters are correlated.
For example, the solubility of U and Pu may be correlated
  They are both functions of pH and other chemical conditions.
  Hence, it may be physically impossible to have a high U solubility and a low Pu solubility.
Two ways to correlate:
  Correlation coefficient (difficult)
  Explicitly represent the reason for the correlation (better)
Notes: Source8_Correlation

## Slide 21: Simulating Complex Diffusive Geometries
A single diffusive mass flux link between two pathways mathematically represents a one-dimensional diffusive process.
However, by appropriately defining the size, diffusive areas and diffusive lengths, you can represent more complex geometries.

## Slide 22: Simulating Complex Diffusive Geometries
Total Volume of Cell2 = (L*π * R2^2)-(L*π * R1^2)
Diffusive Area between Cell1 and Cell2 = 2 *π*R1*L)
Notes: Source9_Cylindrical_Diffusion