## Slide 1: Advanced Water Quality Modeling Concepts
Rick Kossik

## Slide 2: Outline
Modeling Solubility Constraints
Modeling Water Treatment
Modeling Transport on Suspended Solids
Managing Rapidly Changing Cell Volumes (e.g., Cells going dry)
Modeling a Diffusive Barrier
It is assumed you are already familiar with the basic concepts of the Contaminant Transport Module

## Slide 3: Modeling Solubility Constraints
We can model solubility constraints in a simple way in GoldSim.
Although this is not equivalent to modeling the actual geochemical behavior of complex systems, it is appropriate for many applications.
What we can do is specify a solubility limit for each species (actually each element).
GoldSim will not allow the concentration to exceed that value. If the mass in a Cell causes the solubility to be exceeded, the mass precipitates out of solution.
  GoldSim keeps track of the precipitated mass.

## Slide 4: Example: Flushing a Cell with Solubilities
Initial Mass of three species in a Cell.
Each species has a different solubility limit.
Cell has an advective connection that flushes out the mass.
Notes: Solubility1

## Slide 5: Modeling Solubility Constraints
Solubilities can be specified as mass/volume or mol/volume (recall that each species has a molecular weight defined).
We specified solubilities as species properties; but they are actually elemental properties (discussed in next session).
Solubilities often vary throughout the environment.
  To model this in GoldSim, we clone the Reference Fluid.

## Slide 6: Example: Spatially Variable Solubility
Same as previous model.
Mass flushes into a downstream Cell that has different solubility limits (two different “environments”.
Notes: Solubility2

## Slide 7: Modeling Water Treatment
GoldSim provides two ways in which you can simulate a treatment process:
  Precipitate Removal (precipitated mass is rapidly removed from a Cell)
  Treatment Fraction (a specified fraction of the incoming mass to a Cell is removed)
These require use of specialized mass transfer connections.

## Slide 8: Example: Precipitate Removal
Fe and Mg enters Treatment Tank from upstream at a concentration at 1 mg/l.
Treatment tank conditions cause precipitation.
  Fe solubility = 0.01 mg/l
  Mg solubility = 0.1 mg/l
Notes: Precipitate_Removal

## Slide 9: Example: Treatment Fraction
Fe and Mg enters Treatment Tank from upstream at a concentration at 1 mg/l
Treatment tank conditions cause removal of
  99% of incoming Fe
  50% of incoming Mg
Key point: Only Normal links are removed (Coupled links are not)
Notes: Treatment_Fraction

## Slide 10: Modeling Transport on Suspended Solids
You can specify that a suspended solid (with a particular concentration) is present in a pathway.
Mass must partition onto the solid.
The suspended solid is assumed to advect with the fluid in advective connections:
    Flux = Q Cdissolved (1 + K Csolid)
GoldSim does not track the mass of solid itself (just as it does not track advecting fluids).

## Slide 11: Example: Transport on Colloids
Three species: X, Y, Z
Colloids moving with groundwater
Z partitions onto colloids (other two do not)
X and Z partition onto porous medium (other two do not)
Notes: Aquifer_Colloids

## Slide 12: Managing Rapidly Changing Volumes
The GoldSim solution algorithm assumes that the volume of the Cell does not change significantly over a timestep and/or go completely empty.
But in some cases, this will not be the case (e.g., a pond completely drying out).
Under these circumstances, it is necessary to take some special measures to ensure accuracy of the solution.
If we don’t take these special measures, GoldSim will incorrectly compute the concentrations.
To keep things in perspective: if a pond really is drying out, the chemistry itself is likely to be very difficult to model correctly!

## Slide 13: Example: Emptying Cell
Water enters tank at constant rate
  Water entering the tank has a fixed concentration of 100 mg/l (this is also the initial concentration in the tank)
Water flows out of tank initially at a higher rate than the inflow (causing the Cell to empty).
Water then flows out of tank at lower rate than the inflow (causing the Cell to refill)
Notes: Empty_Cell

## Slide 14: Managing Rapidly Changing Volumes
What is causing the spikes?
  The first spike is related to the Cell volume changing significantly over a timestep (> 10%). GoldSim incorrectly computes the concentration in this case.
  The second spike is due to the Cell going completely empty. A small amount of mass is left inside; and mass is still entering (inflow = outflow), but mass cannot leave because GoldSim cannot compute a concentration. So the mass builds up and then is suddenly released when the Cell starts to refill.
In both cases, GoldSim displays warning messages.
Detailed explanations for these errors are provided in Appendix B.

## Slide 15: Managing Rapidly Changing Volumes
How can we address this?
There are two approaches that can address this:
  The first approach is very simple and will apply for most situations.
  The second approach is required if you have rapidly decaying and ingrowing species and/or are modeling isotopes.

## Slide 16: Managing Rapidly Changing Volumes
Approach #1
  Appropriate for most water management applications in which there is no rapid decay and no isotopes. In these cases, a lower solution precision setting can be used (and this modifies how changing volumes are treated).
There are only two changes required:
  Run the model at Low Precision.
  Define a small (but non-zero) Lower Bound for the Cell.
Notes: Empty_Cell_Corrected1

## Slide 17: Managing Rapidly Changing Volumes
Approach #2
  Required for applications in which there is rapid decay and/or multiple isotopes being simulated. In these cases, we want to take advantage of using a higher solution precision setting.
There are two changes required:
  Define a small (but non-zero) Lower Bound for the Cell.
  Dynamically adjust the timestep so that the Cell volume does not change by more than a small amount in a given timestep (e.g., 1%).
Notes: Empty_Cell_Corrected2

## Slide 18: Modeling a Diffusive Barrier
Most contaminant transport models are dominated by advection.
However, there are some situations where diffusion can become important:
  In radioactive waste management models, the time scales are very long, and the engineered system often actually includes diffusive barriers (e.g., a bentonite buffer surrounding the waste).
  In some models, we may intentionally add a diffusive barrier to try to impact water quality. We will explore such an example.

## Slide 19: Example: Diffusive Sediment Barrier
Contaminated layer at bottom of pond. Pond is initially at equilibrium with contaminated layer.
Pond is flushed at constant rate.
Goal is to add a sediment layer on top of the contamination to limit concentration in pond.
Notes: Sediment_Diffusion_No_Sediment, Sediment_Diffusion