## Slide 1: Advanced Container Features Localization, Looping, Conditional, Internal Timesteps and Clones
Rick Kossik

## Slide 2: Advanced Container Features
Localizing Containers
Conditional Containers
Looping Containers
Internal Timesteps
Protecting Containers
Cloning Containers

## Slide 3: Types of Containers

## Slide 4: Localizing Containers
Element ID’s can only be duplicated if they are within different scopes.
You create different scopes by localizing Containers.
You can recognize a localized Container:
  the “arrow” is red
  default symbol in graphics pane is “closed”
  icon in browsers is filled
Can only globalize a Container if it causes no naming conflicts

## Slide 5: Referencing Outputs in a Localized Container
Outputs can only be “seen” inside the Container, unless they are exposed
Once exposed, it is referenced as: ContainerID.OutputID
You can expose an output in several ways. Most common:
  any outputs referenced outside the Container when it is localized are exposed (automatic)
  When selecting an output using the Insert Link dialog
  Manually using the output’s context menu

## Slide 6: Why Localize?
Allows Element IDs to be used multiple times in the same model.
  This allows similar systems to use common variable names.
  Allows systems to be copied and pasted within the same model.
Allows multiple people to work separately on a model.
  Separately developed Containers are simply pasted into a “parent” model.

## Slide 7: Looking INTO a Localized Container
dd
X
X
Exposed on C2
C2 (Localized)
3*C1.X
3*X
3*X
Error
3*X
3*C2.X
Exposed on C1
C1 (Localized)
Notes: Local

## Slide 8: Looking INTO a Localized Container
dd
X
X
Exposed on C2
C2 (Localized)
3*C1.X
3*C2.X
What if I want to reference the X inside C2 from here?
Exposed on C1
C1 (Localized)
Exposed on C1
3*C1.X_in_C2

## Slide 9: Looking OUT FROM a Localized Container
dd
X
X
C2 (Localized)
3*X
C1 (Localized)
X

## Slide 10: Conditional Containers
Containers can be conditional
A conditional container can be active or inactive
If inactive, all of its contents are inactive
Before becoming active, an element propagates zero (except constant Data elements)
When activated, initial values are applied
After becoming inactive, an element continues to propagate its last output value(s)
You determine the circumstances under which the Container activates and deactivates using triggers
Notes: ConditionalContainerProject, ConditionalContainer_Alternative

## Slide 11: Looping Containers
In some models, you may want to carry out an iterative calculation at each timestep. This might be useful, for example, if you have a coupled system of equations that must be solved every timestep by iterating.
The elements inside the Container are updated as follows during the loops:
  On the first loop, the elements are moved forward in time to the next scheduled timestep;
  On subsequent loops, the elements are updated again without advancing time.
Hence, in order for the loops after the first to have any impact on the model, they must contain at least one state variable that changes with each loop.
  A Previous Value element or a Stock
In some cases, iterative calculations like this may be easier in a Script
Notes: Looping Container

## Slide 12: Internal Timestep
In some situations, you may wish to use different timesteps in different portions of your model. This is useful, for example, if the processes represented in one portion of your model occur rapidly and hence require a small timestep to model accurately, while processes represented in the rest of your model occur much more slowly, such that a larger timestep can be used.
GoldSim allows you to assign a timestep that is smaller than the “global” timestep to one or more Containers. For example, your model could have a 10-day “global” timestep, but you could assign a 1-day timestep to a specific Container
Notes: Internal Clock

## Slide 13: Protecting a Container
In some situations, you may want to protect a Container from being edited.
GoldSim provides two mechanisms to do this:
  Sealing
  Locking

## Slide 14: Cloning a Container
In some models, you may wish to create copies of elements which always have identical input strings
To facilitate this, GoldSim allows you to create clones of elements
  If you edit the inputs to one clone, all clones are affected
    All settings and input strings (numbers, expression, links) are identical for all clones
    Names, Descriptions, Save Flags, and Graphical Properties are not cloned
  A Clones tab is added to the element editing dialog to identify all clones
You can clone an entire Container
Why?
  Input data appears where it is used AND in a top level “inputs” Container
  You want to build a function (a subroutine) that is used in multiple locations that you may need to change
Notes: Cloning_MineWaterBalance, Cloning_Subroutine

## Slide 15: Cloning a Container to Use a Subroutine
dd
Z
A
System3 (Localized)
B
dd
Z
A
Subroutine (Cloned)
Complex Calculations
System1 (Localized)
B
dd
Z
A
System2 (Localized)
B
Subroutine (Cloned)
Complex Calculations
Subroutine (Cloned)
Complex Calculations

## Slide 16: Summary
All realistic models should use localized Containers!
Conditional Containers are useful for representing alternative conceptual models and projects.
Looping and Internal Clock Containers are powerful, but rarely required.
You can protect a Container to prevent it from being edited.
Cloned Containers can be useful if you have lots of parallel, identical calculations.