## Slide 1: Simulating Feedback Control Systems Using the New Controller Element
Rick Kossik

## Slide 2: Active Feedback Control
The goal of a feedback control system is to control the value of some variable in the system (e.g., a water level in a pond) by actively adjusting additions (inflows) or withdrawals (outflows) with the goal of dynamically maintaining a desired target value.
This is typically referred to as closed-loop feedback control, and while originally developed to control industrial processes, it also has applications in many other arenas, such as computer engineering, operations research and life sciences (e.g., many natural biological processes are controlled in this way).

## Slide 3: Active Feedback Control
Common Examples:
  You might want to control the water level in a pond (that is receiving rainfall and is evaporating) by turning on and off pumps that add or subtract water from the pond.
  You might want to control the temperature in a house by turning on and off the furnace (i.e., a thermostat is an example of a Controller).
  You might want to maintain a particular inventory level of some item by modifying the production rate up or down.
In the examples in this session we are going to focus on using active feedback control to control the water volume (or water level) in a pond by adjusting inflows and outflows.
Note: We often see badly designed feedback control systems in models!
Notes: Feedback Control

## Slide 4: The Controller Element
Feedback control can be programmed using standard GoldSim elements. But the Controller element makes it much easier to do so.
Controllers use feedback control to influence the state of a process and adjust it to a desired value (a target). A process could conceptually involve something quite complex (e.g., an entire chemical plant), but typically will be something much more specific (e.g., a single tank in that plant).
The state is some property of the process that we want to control (e.g., the volume of water in the tank). The state is referred to as the process variable. In GoldSim, the process variable is usually the main output of a Pool or Reservoir (and hence a state variable).
Notes: Show Controller Element

## Slide 5: The Controller Element
Controllers produce a single output (which is always a flow).
This flow is then intended to be connected back to the process (e.g., a Pool element representing the volume of water in a tank) in order to adjust the value toward the target.
The Controller requires as input a process variable (which will typically be the primary output of a Pool or Reservoir) and in turn produces a flow that is then directed back to impact that process variable (e.g., an inflow or an outflow to the Pool or Reservoir defining the process variable).
This forms a feedback loop.

## Slide 6: Active Feedback Control
Process (e.g., a pond)
Process Variable(s) (e.g., Water Volume)
Controller
Controller Output (e.g., Requested Outflow)
Target (e.g., Desired Water Volume) and Other Parameters for Controller

## Slide 7: The Controller Element
Controllers are defined as either Inflow Controllers or Outflow Controllers.
Inflow Controllers increase the process variable (in response to the process variable decreasing). The output of an Inflow Controller is intended to be used as an inflow to the process (e.g., an inflow to the Pool or Reservoir being controlled.
Outflow Controllers decrease the process variable (in response to the process variable increasing). The output of an Outflow Controller is intended to be used as an outflow to the process (e.g., an outflow to the Pool or Reservoir being controlled.
Many systems will have both Inflow and Outflow Controllers.

## Slide 8: The Controller Element
Controllers can act in a discrete manner (turning a flow on or off when specified conditions are met), or in a continuous (or near continuous) manner, constantly adjusting flows every timestep.
In some cases, we may indeed want to represent those various discrete actions as “events”. A thermostat is an example of such a Controller.
In other cases, we want to continuously adjust the flows.
  This could represent that actual near continuous adjustment of flow rates.
  More commonly in water resource models, we are trying to represent the lumped effect of the discrete actions of the system’s operators (people) over the simulated timestep (e.g., 1 day). That is, we typically are not simulating the discrete actions themselves, only their lumped effect (which over the timestep appears continuous).

## Slide 9: Basic Controller Inputs
Flow Units: These are the display units for the output of the Controller. Must be a flow rate of some kind.
Quantity Units: These are the display units for the Process Variable and the Target. They must “match” the Flow Units in that they must have dimensions of the Flow Units times Time.
Process Variable: This is the variable that is being monitored and controlled by the Controller.
Flow Direction: Either “Inflow” or “Outflow”.
Flow Capacity: This is the maximum value that the output of the Controller can take on. It is typically associated with some physical limitation (e.g., the size of a pump).

## Slide 10: Controller Methods
Controllers have three different (user-selected) control methods by which they determine how the Controller output is computed.
Depending on the method selected, the required inputs will change.
Methods:
  Deadband
  Proportional
  Proportional Integral Derivative (PID)

## Slide 11: Deadband Controller
A Deadband Controller produces an output that switches abruptly between two states: a specified flow (the Flow Capacity) or zero flow.
This is how a simple thermostat works. A thermostat monitors temperature (a proxy for heat, which is a state variable).
In this example, since we are adding heat (there is an inflow of heat), this is an Inflow Controller.

## Slide 12: Defining a Deadband Controller
Two ways to define a Deadband Controller
Top and Bottom
  Top of Deadband
  Bottom of Deadband
Target and Thickness
  Target
  Thickness
  Target Position (Center, Top, Bottom)
Also need to define the Initial Flow State
  If initial value is withing the deadband, is the flow operating?
Notes: Deadband

## Slide 13: Behavior of a Deadband Controller
Deadband Controllers result in a process variable the oscillates between the bottom of the deadband and the top of the deadband.
  The smaller the deadband (and the higher the Flow Capacity), the more frequent the oscillations.
The process variable does not necessarily stay within the dead band.
  Might take some time to counteract the uncontrolled flows
If the process variable is a state variable, GoldSim inserts a timestep when the boundary of deadband is reached. If it is not a state variable, the boundary is evaluated every scheduled timestep.
  Hence, if state variable, behavior is independent of scheduled timestep length.

## Slide 14: Proportional Controller
For a Proportional Controller, the output response is proportional to the current error:
  Output = Bias + Proportional Gain * Error
Error definition depends on type of Controller:
  Outflow Controllers: Error = Process Variable – Target
  Inflow Controllers: Error = Target – Process Variable
In addition:
  The output cannot be less than zero.
  There is a maximum value for the output (Flow Capacity).

## Slide 15: Defining a Proportional Controller
For a Proportional Controller, we need the following:
  Target: Desired value of process variable
  Bias: This is the value of the output when the error is zero. For example, if this is an Outflow Controller, the Bias can be thought of as the sum of the expected uncontrolled inflows minus expected uncontrolled outflows. That is, if the process variable was at the target, what would the flow need to be to maintain it at the target.
  Proportional Gain: This has dimensions of inverse time, and represents how strongly the Controller responds to the error. The larger this number, the quicker it responds.
Notes: Proportional

## Slide 16: Behavior of a Proportional Controller
Unlike Deadband Controllers, they respond continuously (every timestep).
Work well if the expected uncontrolled inflows and outflows do not have a significant trend or pattern (such that a constant Bias can be easily specified to match them).
Impacted by timestep (smaller the timestep, more frequently flow is updated).
If the uncontrolled inflows and outflows follow a trend or pattern, Proportional Controllers (with a constant Bias) result in poor performance.

## Slide 17: Defining a Time-Variable Bias
The Bias can be thought of as the sum of the expected uncontrolled inflows minus expected uncontrolled outflows. Instead of defining a constant Bias, we could define a time-variable Bias that represents a forecast of the uncontrolled flows.
One nice aspect of this approach is that it probably represents what is often informally done (“the current level is too high AND the inflows have been high recently due to the weather; let’s increase pumping”).
One common and simple forecast method is exponential smoothing, which can be easily implemented using an Information Delay.
If we do this, the Proportional Controller works quite well even if the uncontrolled inflows and outflows follow a trend or pattern
Notes: Proportional_Forecast

## Slide 18: PID Controller
For a PID Controller, the output response is proportional to the current error:
  Output = Bias + Proportional Gain * Error
Error definition depends on type of Controller:
  Outflow Controllers: Error = Process Variable – Target
  Inflow Controllers: Error = Target – Process Variable
In addition:
  The output cannot be less than zero.
  There is a maximum value for the output (Flow Capacity).

## Slide 19: Defining a PID Controller
For a Proportional Controller, we need the following:
  Target: Desired value of process variable
  Bias: This is the value of the output when the PID Sum is zero.
  Proportional Gain: This has dimensions of inverse time, and represents how strongly the “P” term responds to the error. The larger this number, the quicker it responds.
  Integral Gain: This has dimensions of inverse time squared, and represents how strongly the “I” term responds to the error. The larger this number, the quicker it responds.
  Derivative Gain: This is dimensionless, and represents how strongly the “D” term responds to the error. The larger this number, the quicker it responds.
If Integral Gain and Derivative Gain are zero, PID Controller becomes a Proportional Controller
Notes: PID

## Slide 20: Behavior of a PID Controller
Responds continuously (every timestep).
Impacted by timestep (smaller the timestep, more frequently flow is updated).
Works well even if the expected uncontrolled inflows and outflows have a significant trend or pattern.

## Slide 21: Comparing Methods
Deadband: Very flexible. Performs well. Can oscillate. Often matches the actual physical process well (e.g., thermostat).
Proportional: Performs well if uncontrolled flows are relatively constant.
PID: Performs well under almost all conditions. Multiple tuning parameters
Proportional with Time-Variable Bias: Performs well under all conditions. Can take some effort to collected uncontrolled flows.
Notes: Compare Controllers

## Slide 22: Defining a Target that Represents an Upper or Lower Limit
In many cases, the goal is to control the process variable around a target level (e.g., a thermostat).
In others the goal may be to control the target level as it approaches an upper or lower limit.
  There may be a hard or soft limit below or above which the process variable cannot go.
We can readily represent this by setting the target to the upper or lower limit
Notes: Target at Lower Bound, Multiple Outflows

## Slide 23: Multiple Controllers
In these examples, we have only considered uncontrolled inflows and using a single outflow to control the water level.
You will often have multiple Controllers. Let’s look at an example first with multiple outflow Controllers.
You can also have both uncontrolled inflows and outflows and hence may need to use both inflows and outflows to control the water level.
Notes: Inflow Outflow

## Slide 24: Using a Proxy for the Process Variable
The process variable and the output of the Controller must have consistent dimensions (e.g., m3 and m3/day).
In some cases, however, your target will not be defined in the same units as the process variable.
  Target is temperature, not heat
  Target is water elevation, not volume
In these cases, the targets are proxies (e.g., water elevation) that then need to be converted (e.g., to volume).

## Slide 25: Using a Proxy for the Process Variable
In some cases, the conversion factor is simply a constant
  Water level in a tank to volume
Notes: Proxy

## Slide 26: Using a Proxy for the Process Variable
In other cases, the conversion factor is not a constant
  Water level in a pond to volume
  Requires a lookup table

## Slide 27: Controllers Can be Turned On and Off
Can be used to simulate:
  Equipment failures
  Control logic
Notes: Controller On Off

## Slide 28: Summary
Active feedback control systems commonly need to be simulated.
The new Controller element makes it easy to represent such systems in a realistic and powerful way.
The Controller provides different methods for responding to changes in the process variable. Which one is best for your situation will require experimentation (and tuning). Use the easiest method that meets your needs.