## Slide 1: Phone numbers for tonight
Rick Kossik: 425-894-5172
Jason Lillywhite: 425-394-2342
Mark Miller: 206-561-4300

## Slide 2: Introduction to Reliability Modeling in GoldSim
Rick Kossik

## Slide 3: Outline
What is reliability modeling?
What is the Reliability Module?
  Modeling failures (and repairs)
Modeling the consequences of failures
  Linking the Reliability Module to the rest of your model
Some advanced examples

## Slide 4: Reliability Modeling
Reliability modeling involves modeling the ways that systems can fail (and be repaired) in order to help determine how to increase their design life, and eliminate or reduce the likelihood of failures, downtime and safety risks.
The output of these models typically consists of predictions of measures such as reliability (the probability that a component or system will perform its required function over a specified time period) and availability (the probability that a component or system is performing its required function at any given time).

## Slide 5: Why Do Reliability Modeling?
Reliability and availability may sometimes be of interest themselves (e.g., a system might need to meet a certain specification).
More importantly, reliability and availability ultimately affect system performance (e.g., throughput, warranty costs and/or maintenance costs).
Moreover, failures can result in serious (and sometimes catastrophic) consequences.
Reliability modeling can be used to identifying key sources of unreliability and subsequently help design systems that improve performance.

## Slide 6: How is Reliability Modeling Carried Out?
Traditionally, modeling approach is typically simplified (e.g., static), often using closed-form solutions and other analytical approaches.
GoldSim approach is relatively unique, as for historic reasons, simulation is not commonly used.
  Simulation allows for realistic representation of complex dynamics and the consequences of failure.

## Slide 7: Reliability Modeling in GoldSim
Relies heavily on discrete event modeling, since failures (and repairs) are sudden events. You therefore must be familiar with GoldSim’s event modeling features.
The Reliability Module provides two special reliability elements for building reliability models.
The Function element is used to model components that perform their function over time (e.g., a pump or a battery).
The Action element is used to model components that perform their action instantaneously (e.g., a switch or a relay).

## Slide 8: Reliability Elements
Each reliability element can exist in a number of different states, such as:
Operating: turned on and not failed or undergoing maintenance
Failed (the element has an unrepaired failure mode)
Inoperable because some other requirements are not met (e.g., its power supply is unavailable)
Undergoing maintenance
Off: turned off
Each of these states corresponds to a code (a status) that is output by the element (an integer)

## Slide 9: The Status Output
Status | Definition | Name
0 | Operating | RL_Operating
1 | Preventive maintenance underway | RL_PM
2 | Failed | RL_IntReqFail
3 | External requirement unmet | RL_ExtReqFail
4 | Off | RL_Off

## Slide 10: Example: Failure of a Pump
  The pump has a failure rate of once per 3000 hours of operation
  We will simulate the system for 90 days
  Now let’s assume that the pump is turned off between midnight and 8AM
Notes: Simple_Failure and Simple_Failure2

## Slide 11: Example: Including Multiple Failure Modes
  Assume is always operating (no on/off switch)
  The pump has three different failure modes
  We will simulate the system for 90 days
Notes: Failure_Modes

## Slide 12: Example: Modeling Repairs
  When the pump fails, it is repaired
  Repair time is a function of the failure mode
Notes: Repairs

## Slide 13: Example: Modeling a Backup System
  Two pumps
  When the first pump fails, it activates (turns on) a backup pump
  When the first pump is repaired, the backup pump is turned off
  The process of activating the backup pump is not perfect (it can fail)
Notes: backup

## Slide 14: Modeling Systems
In the previous example, we modeled each pump
What we ultimately care about, however, is the performance of the system of pumps
Most real-world problems involve systems of components
  a computer is a system consisting of a CPU, a power supply, a hard drive, memory, etc.
  a car is a system consisting of an engine, a transmission, a fuel system, etc.
    An engine itself is a system consisting of pistons, etc.
GoldSim provides powerful tools for modeling systems of components
Notes: Backup_system

## Slide 15: Other Common Types of Systems
The system we just looked at was a parallel system
Other systems are series
Or more complex:
GoldSim can easily represent any of these systems
Notes: Series, complex1, complex2

## Slide 16: Modeling External Requirements
Sometimes systems have external requirements in order to operate.
Returning to the backup pump system, let’s add a generator and fuel to the model…
Notes: Backup_System_External

## Slide 17: Advanced Features
Failure can be a function of different “control variables”:
  Operating time (default)
  Total time (accrues time even if the element is off)
  Number of Actions completed
  Custom (e.g., mileage)
For processes that depend on the operating environment, GoldSim supports the use of acceleration factors that can dynamically change the failure rate in response to environmental conditions.
You can model preventive maintenance

## Slide 18: Modeling the Consequences of Failure
Reliability and availability may sometimes be of interest themselves (e.g., a system might need to meet a certain specification)
More importantly, reliability and availability ultimately affect the performance of your model itself (e.g., water levels in a pond)
We link the rest of a model to the reliability elements by referencing their status

## Slide 19: The Status Output
To reference if the element “Pump” was operating, you could write either of the following conditional expressions (e.g., in a selector or expression):
  Pump = 0
  Pump = RL_Operating
Status | Definition | Name
0 | Operating | RL_Operating
1 | Preventive maintenance underway | RL_PM
2 | Failed | RL_IntReqFail
3 | External requirement unmet | RL_ExtReqFail
4 | Off | RL_Off
Notes: Pump_Throughput, Pond, Overtop

## Slide 20: Some More Complex Applications
Closed circuit grinding mill, used in many mine processing plants. There are 3 mills are available, and the process requires at least 2 be operating at any one time to maintain the required production rate.
An unmanned planetary mission.
Notes: Grinding_Mill_Circuit, Orbiter

## Slide 21: Learn More
Experiment with the Reliability Module
  All GoldSim copies have a “Learning Edition” of the Reliability Module that allows up to 10 reliability elements. This is sufficient to experiment with and often build real models
Read Reliability White Paper
Read Reliability User’s Manual
  Relatively short and includes lots of examples