## Slide 1: Simulating Climate Change Uncertainty in GoldSim
By: Dave Hoekstra
SRK North America
With special thanks for the assistance from:
Victor Munoz for helping me understand Climate Change
Assaf Wunsch for demonstrating Power Query Data reduction
Justin Eisner for creating our custom Python tools

## Slide 2: Why do we have to include climate change??
Designing new mines needs to include long-term closure in the design
The mining industry understands:
  Permanent and safe closure is needed
  Risk-based approaches is needed
  Agencies and industry group guidance and support (ie. GISM)
  Closure (for perpetuity) must include climate change
Best shot is to do right the first time
Redo’s are expensive when the source of funding is gone
Notes: SRKs primary business is the mining industry, and a big part of that is designing new mines for including long-term closure in the design
The mining industry is strongly driven by the need to permanently and safely close and reclaim tailings facilities
  Industry understands and incorporates risk-based approaches
  Many guidance documents by agencies and industry groups
  Global Industry Standard on Tailings Management (GISTM) is very relevant and says you must include climate change
There is one chance at the end of mining to do this economically and with the best knowledge of site conditions
  Must be designed for perpetuity – redo’s are expensive when the source of funding is gone

## Slide 3: What we need to address with Climate Change
Understand the impacts on the Facility, the Environment, and Community
Resilient to climate change risks - Principles of risks are ALARP*
Monitor and adapt as conditions change
Set aside funding during active mining for closure costs
*ALARP: as low as reasonably practicable
Notes: Understand the impacts of climate change on the functioning of the facility, the environment, and stakeholders
Design facilities that are sufficiently resilient to climate change risks through all lifecycle phases, including post-closure, following principles of ALARP* risk
Monitor and regularly review the data and resulting impacts, and adapt the design and operation to suit
Funding should be allocated at the initial design and set aside during active mining for closure CAPEX and OPEX

## Slide 4: Climate Change Background
Lets go over the basis so we are all on the same page:
Temperatures has increased historically beyond past conditions.
Hydrologist used to assume
Future conditions = Past conditions
This is no longer a valid assumption for future conditions
Temperature beyond historical => Predictive climate modeling
Source: Victor Munoz (SRK Vancouver)
Notes: Temperature has increased historically beyond past conditions.
Typical hydrology and meteorology approaches assume past conditions are representative of future events
  This is no longer a valid assumption for future conditions

## Slide 5: General Background- General Circulation Models
Climate change predictions : Assessment Reports from the Intergovernmental Panel on Climate Change (IPCC)
Best understanding of climate modeling at that time
  Issued every 5 to 10 years (1990, 1995, 2001, 2007, 2022)
  The General Circulation Models (GCM) predict future conditions up to 2100.
  Include interaction of a host of climate influencing factors
  Each can produce results for a single grid (i.e. project site)
  34 different GCMs are available. Each has different methods and assumptions
  Comparison of the different GCMs is the Coupled Model Intercomparison Project (CMIP)
Notes: Climate change predictions are addressed in regular Assessment Reports prepared by the Intergovernmental Panel on Climate Change (IPCC)
Each Assessment presents best understanding of climate modeling at that time
  Issued every 5 to 10 years (1990, 1995, 2001, 2007, 2022)
  The General Circulation Models (GCM) extend present conditions into the future conditions up to 2100.
  Include interaction of a host of climate influencing factors
  34 different GCMs are available to incorporate different methods and assumptions, not all are applicable to every Point / Parameter / Climate Scenario
  The comparison of the different GCMs to find consensus is the Coupled Model Intercomparison Project (CMIP)

## Slide 6
Scenarios
Each GCM incorporates a series of Scenarios
  Estimates the heat in balance within the planet (radiative forcing) by the year 2100
Different scenarios are paths we take to reach some heat level or Representative Concentration Pathways (RCPs)
The RCP is an indication of the amount of temperature change expected
TL/DR ► RCP is an END condition for 2100 y how hot will it get in 2100
Notes: Each GCM incorporates a series of scenarios, which account for different assumptions about the amount of heat in balance within the planet, or radiative forcing (W/m2) in the atmosphere by the year 2100
Different scenarios represent the pathway we assume we will take to reach a heat level or Representative Concentration Pathways (RCPs), from 2.6 (less heat) to 8.5 (most heat)
The RCP is an indication of the amount of temperature change

## Slide 7: Shared Socioeconomic Pathways
SSP1 | Sustainability – Taking the Green Road (Low challenges to mitigation and adaptation
SSP2 | Middle of the Road (Medium challenges to mitigation and adaptation) This future poses moderate challenges to mitigation and moderate challenges to adaptation Population growth stabilizes toward the end of the century Current social, economic, and technological trends continue Global and national institutions make slow progress toward achieving sustainable development goals
SSP3 | Regional Rivalry – A Rocky Road (High challenges to mitigation and adaptation)
SSP4 | Inequality – A Road Divided (Low challenges to mitigation, high challenges to adaptation)
SSP5 | Fossil-fueled Development – Taking the Highway (High challenges to mitigation, low challenges to adaptation) This future poses high challenges to mitigation and low challenges to adaptation Global population peaks mid-century Emphasis on economic growth and technological progress Global adoption of resource and energy intensive lifestyles Lack of environmental awareness
TL/DR ► SSP y how do we get there?
Scenarios also cover the way our society will address land use and greenhouse gases emissions
Span a wide range of future outcomes through 2100
Notes: Scenarios also cover the pathways of land use and emissions of air pollutants and greenhouse gases that spanned a wide range of future outcomes through 2100

## Slide 8: Projection Periods
GCMs provide historical baseline results from 1900 through 2014 and projections out to 2100
GCM model results often grouped in 30-year chunks for climate normals.
  2020’s (2011-2039)
  2050’s (2040-2069)
  2089’s (2070-2099)
GCMs don’t predict past 2100, and should not be “straight lined” beyond that
  No basis to believe these trends could continue for 100’s of years
Projections beyond 2100 are not typically presented – so what does design for perpetuity mean?
Notes: Models provide historical baseline results from 1900 through 2014 and projections from 2030 through 2100
Typically, GCM model results are grouped in 30-year chunks based on WMO suggestions for climate normal.
  2020’s (2011-2039)
  2050’s (2040-2069)
  2089’s (2070-2099)
The model do no predict past 2100, and should not be “straight lined” beyond that
  No basis to believe these trends could continue for 100’s of years

## Slide 9: General background – Baseline and Anomaly
Baseline is the period to be compared with other future periods. In this case baseline (base) is considered between 1951 to 1980.
Anomaly is considered the difference with respect to a baseline period
Baseline values are typically annual averages against the 30-year baseline average as reported by the model
Temperature Anomalies are typically described as Δ Temperature from Baseline
  Δ Tavg = Temperature – Baseline Temperature (± °C)
Precipitation Anomalies are typically described as relative change from baseline
Notes: Baseline is the period to be compared with other future periods. In this case baseline (base) is considered between 1951 to 1980.
Anomaly is considered the difference with respect to a baseline period
Baseline values are typically annual averages against the 30-year baseline average

## Slide 10: Background – TL/DR
Terminology is important and we love our jargon
Concept | Meaning | It really means…
IPCC | Intergovernmental Panel on Climate Change | International body that produces the models used for climate change predictions
RCP | Heat balance of the planet in the year 2100 | How hot will the planet get by 2100
SSP | 5 different pathway to year 2100 of land use, population growth, greenhouse gas emissions, etc. for the whole planet | How will society respond to climate change
Baseline | Baseline temperature and precipitation | Climate in the end of the last century
Anomaly | Difference in precipitation or temperature from a baseline value | Change from baseline
AR{X} | Assessment Report Number {X} | Identify which climate study report (issued about every 5 yrs)
GCM | General Circulation Model | Single Climate Prediction Model
CMIP | Coupled Model Intercomparison Project | Comparison of multiple Climate Prediction Models
Projection Period | Multi-decade block to evaluate climate change anomalies within a window of time | Break down climate change into 30-year windows

## Slide 11: What anomaly to use to predict Climate Change
We don’t know which GCM is the right one
  Select the average anomaly for all the models
  Reasonably conservative given the lack of knowledge of the future
Especially appropriate if we will get a chance to observe conditions and correct our design
If we only have one chance to do it right (closure design for perpetuity today), we should be more conservative and explore the whole range of climate change response
Notes: There is no way to determine which GCM is the right one, so climate change predictions will usually select the average anomaly for each Projection Period and each Scenario you wish to include
Reasonably conservative given the lack of knowledge of the future
Appropriate when we expect to have the opportunity to see how society responds (SSP) or which assumptions and methodologies prove to be better (GCMs)
If we only have one chance to do it right (closure design for perpetuity today), we should be more conservative and explore the whole range of climate change response

## Slide 12: Understanding the Uncertainty in the GCMs
Must evaluate each Scenario separately SSP-2 ≠ SSP-5 – cannot be combined
For any given scenario, what is the range of the anomaly predictions for all the GCMs?
In the Box and whisker plot, 50% of the results (25% to 75%) will show up in the box, and any points outside ~3 sigma will show up outside the whiskers

## Slide 13: What does the Uncertainty look like?
4 Scenarios (SSP & RCP)
Up to 34 Models within each Scenario
Typically, 3-4 Projection Periods
Every GCM has their own “Path” that is a function of individual assumptions and boundary conditions
As each GCM is equally likely, the average of all the GCMs is a reasonable assumption
All the average annual GCM temperatures
Average SSP2 4.5 Temperature
Single GCM temperature path (NESM3 SSP2 4.5)

## Slide 14: Scatter Plot of Relative Change through Time
Any scenario is in fact a cloud of 25-34 different GCM results.
Plotting Temperature and Precipitation anomalies for a single scenario through 4 Projection Periods

## Slide 15: GCM Uncertainty
The cloud of uncertain expands as we include more models, more scenarios, and farther projections

## Slide 16: Making it happen in GoldSim
aka - What am I doing in this handbasket?

## Slide 17: WGEN distribution fitting
Goldsim has a long history of using the WGN model for a daily stochastic climate generator
The original WGEN model (Richardson & Wright, 1984) works with a static climate model – i.e. mean temperatures don’t change
Climate simulation must be dynamic but simpler than the GCMs
WGENs Precipitation model assumes the non-zero precipitation distribution is a 2-parameter gamma
  Only needs mean and std deviation, very easy to fit
  Sometimes, other distributions will fit better.
Johnson SB distribution
(Source: reference.Wolfram.com)
Notes: The original WGEN model (Richardson & Wright, 1984) works with a static climate model – mean temperatures doesn’t change
  This is no longer valid, and climate simulation must be dynamic, without the massive detail incorporated into the GCMs
WGENs Precipitation model assumes the non-zero precipitation distribution is a 2-parameter gamma
  Only needs mean and std deviation, very easy to fit
  We have found that depending on the climate, other distributions will fit better.

## Slide 18: WGEN Distribution fittings
Fit the distribution and plot Quantile-Quantile plots (Q-Q plots)
Note that a straight 45° line means the shape of the distribution is correct (e.g. left skew, thickness of tails, etc.)
Wakeby (K.S. 0.2623)
Johnson SB (K.S. 0.3153)
Gumbel Max (K.S. 0.2953)
Gamma (K.S. 0.4763)
Normal (K.S. 0.2726)
Kolmogorov-Smirnov test doesn’t always guide you to the best distribution
Generally, see one of these five give the best results
Notes: Using Mathwave’s EasyFit software (no longer supported) to

## Slide 19: Adjusting WGEN for Climate Change Precipitation
WGEN didn’t account for change over time
SRK will incorporate multiple WGEN parameter sets and can select different distributions over time
  Similar to the Original WGEN, each set contains monthly tables for:
    Probability of Rain day (Pwet-wet and Pwet-dry)
    Fitted parameters for non-zero precipitation distribution
      JohnsonSB distribution (transformed normal): Shape g, Shape d, Scale l , Location x works very well and can be reproduced in GoldSim
Notes: Assume you understand the methods behind WGEN climate generator

## Slide 20: Adjusting WGEN for Climate Change Precipitation
However, each set ALSO contains:
  3D lookup tables for each climate scenario
  Calendar year ‘hinge points’ to project trends
  Separate layers for each GCM data set used
GoldSim linearly interpolates between the hinge points according to the calendar year
KEY ASSUMPTION – adjusting distribution parameters between calendar years results in valid distributions

## Slide 21: Adjusting WGEN for Climate Change Temperature
Dynamic temperature model
Mean annual temperature is adjusted every year, and monthly and daily vary from that basepoint
3D Tables for
  Mean Annual temperature and rate of change
  Annual temperature anomaly from tend mean and Std. Dev.
  Monthly anomaly from annual Mean & Std. Dev.
  Precipitation depth to min and max temperature correlations
  Avg Monthly – daily Min daily temperature anomaly Mean & Std. Dev.
  Daily Max – daily min temperature anomaly Mean & Std. Dev.

## Slide 22: Adjusting WGEN for Climate Change
Model calculates mean annual Temperature from trend lines
Generates an anomaly Δ°C from the mean
Generates monthly temperature anomalies Δ°C from the annual
Generates average daily temperature Δ°C from the monthly average
Generates minimum daily temperature Δ°C below the average daily temperature
Generates maximum daily temperature Δ°C above the daily minimum temperature

## Slide 23: Adjusting WGEN for Climate Change
As mentioned earlier, not every GCM is available for every scenario or parameter
We may also not want to use some GCMs which are outliers in one scenario and valid in another
Within each climate scenario, we define which of the models are valid
GoldSim script dynamically develops a table (similar to the discrete distribution) that allows for any of the available models to be selected with equal likelihood

## Slide 24: Climate Change Incorporation into GoldSim Water Balance Workflow
Identify Climate Change Scenarios to incorporate in the Study
  Typically, SSP-2 RCP 4.5 and SSP-5 RCP 8.5
  Also see SSP-1 RCP 2.6 and SSP-3 RCP 7.0
Download all available files from CIMP
  Daily data from baseline to 2099, at least Tmin,Tmax, Tavg, Precip)
  1985-2099, 31 models, 4 scenarios = 5.2 million lines of data
Determine Projection Periods (capture critical points in time)
Use Microsoft Power Query to format data files
  Time series - baseline through 2099
  By GCM, by Scenario = 124 files

## Slide 25: Climate Change Incorporation into GoldSim Water Balance Workflow
Evaluate precipitation probability distributions (which is the most appropriate fit? – one distribution to rule them all?)
Using custom python tool, develop WGEN parameters for each GCM used
  4-6 monthly precipitation parameters
  3 annual and 3 monthly temperature parameters
  6 parameters for daily minimum and maximum temperatures
  Export to text file for import into GoldSim 3D table
  12 months x 4-5 hinge point years x 25-31 models
    (rows x columns x layers)
  2 to 4 3D lookup tables each, one for each scenario included

## Slide 26: GoldSim Modeling Process
User selects a climate scenario:
  Optimistic: SSP-1 RCP 2.6
  Middle of the road: SSP-2 RCP 4.5 or SSP 3 RCP 7.0
  Pessimistic: SSP5 RCP 8.5
Begin simulation:
  Each realization: Randomly select GCM
  Each Year: Stochastically generate mean annual temperature and monthly tables of precipitation and temperature parameters
  Each Month: Stochastically generate mean monthly temperature and extract daily temperature and precipitation parameters
  Each Day: Stochastically generate daily precipitation depth, minimum, maximum and average temperature

## Slide 27: Generate Cloud of temperature and Precipitation Results
Stochastic Results for SSP-2 4.5 climate predictions, using 7 of the 31 GCM for a site in South America

## Slide 28: Summary
Because future IS uncertain (there are +100 GCM when you include scenarios) then results are not fixed values but ranges.
Climate Projections out to year 2100 can be made using the WGEN stochastic climate generator in GoldSim
For simplicity, these ranges can be presented as median value; however, we may need to understand uncertainty and accept variability for highly conservative designs
The climate change model produces daily precipitation and temperature that can be fed into the hydrologic models
  Rainfall-runoff (GR4J, AWBM, etc.)
  Snowpack/snowmelt (CemaNeige, Snow 17)
These models can then feed the water balance model to predict long-term climate that incorporates the full range of climate change predicted

## Slide 29: Extra Slides
Global Industry Standard on Tailings Management (GISTM) is mandatory by ICMM members (SRK Clients).
  Understand the impacts of climate change on the functioning of the facility, the environment, and stakeholders.
  Design facilities that are sufficiently resilient to climate change risks through all lifecycle phases.
Because future IS uncertain, there are +100 GCM (including scenarios); then results are not fixed values, in-fact these are ranges.
Projections up to year 2100.
For simplicity, these ranges can be presented as median value; however, we need to understand uncertainty and accept variability.
Within SRK, we have supported meteorology and runoff supporting requirements associated to climate change.

## Slide 30: Shift to Assessment Report 6
Standard scenarios, (RCPs)
i.e. How HOT is the planet?
Shared socioeconomic pathways (SSPs) based on evolution of human society in the absence of climate change or climate policy
AR5
AR6
Outcome = matrix of possible integrated scenarios that lead to a final emissions forcing
Notes: Released August 2021
Building on the scenarios developed in previous assessment reports
Applying the change in society, population, technology, economies and political action, in the absence of climate change or climate policy
New scenarios with AR6 combine climate simulations, in terms of radiative forcing in the atmosphere, with societal shift
Allow for analysis of future climate mitigation, adaptation and impacts

## Slide 31: Technical – Bias Correction

## Slide 32: Impact of Climate Change will be very dependent on location
Example output of the rate of change to global runoff rates through 2060
Source: Adapted from Milly et al. 2005

## Slide 33: Confidence Limits of GCM models
Given our lack of knowledge of what will happen in the future, all models are assigned equal likelihood
However, we can use confidence limits to reduce our data processing requirements by eliminating outliers, or only incorporating models that define the extents of the uncertainty
