## Slide 1: A Climate Informed Reservoir Operation Model Anita Johnson Support from Page Weil (LRE Water) and Jason Lillywhite (GTG)
9/11/2024

## Slide 2: Introduction
Who am I and why am I here?!
Presentation Background:
  Great opportunity to build a model that features several cool tools from the GoldSim library.
  I wanted to have a go at simulating climate change
    Most mine-related models will need that in the future
Model Concept:
  Based on a Colorado drainage basin
  Water storage reservoir
  Provide support for reservoir management and planning
  Evaluate risks related to seasonal variability and climate change

## Slide 3: Conceptual model
Objectives:
Build a model capable of day-to-day water rights and reservoir release management
Provide long-term climate-informed drainage basin forecasting

## Slide 4: Model tOOLS
Synthetic climate data generation
  Precipitation (PrecipGen / PrecipGen PAR) - stochastic
  Temperature (TempGen / TempGen PAR) - stochastic
  Evapotranspiration and pond evaporation (Hamon)
  Snow accumulation and melting (CemaNeige)
Catchment runoff rate calibration and prediction
  Australian Water Balance Model (AWBM)
  Pool element
  To allocate available water to outflows based on priority
Scenario manager
  To illustrate climate change alternatives

## Slide 5: Climate Simulation
Historical data
  Precipitation
  Snow Water Equivalent (SWE)
  Temperature (Tmax, Tmin, Tavg)
  Pond evaporation (not sure how they determined this…?!)
Synthetic daily climate data
  Precipitation - PrecipGen
  Temperature – TempGen (min and max)
  Pond Evaporation - Hamon
  Snow accumulation and melting - CemaNeige
Calibrate synthetic climate to historical
Use synthetic for forward part of simulation.

## Slide 6: SYNTHETIC PRECIPITATION tool
PrecipGen/PrecipGen PAR
  Based on the popular climate generator ‘WGEN’ by Dee Allen Wright (1983)
  Enhanced to better represent historical climate cycles
    ~2 year - decades cycles
    Better representation of successive years of drought or deluge
    Improves match to the tails of the precipitation distributions
  Uses a Markov Chain approach
    The probability of a specific event today (rain) depends on what happened yesterday (rain or dry).
  One precipitation generator for each climate scenario

## Slide 7: Precipitation generator Calibration
Methodology
  Run PrecipGen PAR to get input parameters for PrecipGen (these are statistics describing historical data)
  Enter PAR values in PrecipGen
  Configure a timeseries element with historical precipitation data
  Run a 1-year simulation with a generous number of realizations (100?)
  Check the match between simulated and historical data statistics.
  If the match is poor, return to PrecipGen PAR and adjust some calibration parameters.
Monthly Cumulative Precipitation
Cumulative Probability Distribution

## Slide 8: Temperature generator Calibration
TempGen/TempGen PAR
  Based on the popular ‘WGEN’ by Dee Allen Wright (1983) which is based on:
    Matalas (1967)
    Richardson and Wright (1984)
  Works in a similar way to PrecipGen/PrecipGen PAR
    Run TempGen PAR to get input parameters for TempGen (these are statistics describing historical data)
    Enter PAR values in TempGen
    Run a 1-year simulation with a generous number for realizations (100?)
    Check match between statistics associated with simulated and historical data.
Daily Max Temperature Calibration
Daily Min Temperature Calibration

## Slide 9: Snow Water Equivalent Generator Tool
CemaNeige
Valery, A. et. al. ‘As simple as possible but not simpler’: What is essential in a snow-accounting routine? Part 1 – comparison of six snow-accounting routines on 380 catchments. J.Hydrol., 2014.
Spatialization method
Spatialization divides catchment into zones by altitude and temperature to better represent steep catchments
Input parameters
  Daily Precipitation
  Daily Maximum temperature
  Daily Minimum Temperature
  Elevation of the weather station from which the climate data came
  Historical snow water equivalent data (if possible) for calibration
Calibration Parameters
  Precipitation Gradient
  Hypsometry
  Temperature_LapseRate
  Snowpack Inertia Factor
  DegreeDay Factor
Snow Water Equivalent Calibration
(partial)

## Slide 10: Synthetic Evaporation Generation tool
Hamon Method for Estimating Pond Evaporation and evapotranspiration
Inputs
  Site latitude
    To reflect daily number of daylight hours
  Average daily temperature
Pond/Lake evaporation rate calibration

## Slide 11: Catchment Runoff Simulation
Australian Water Balance Model (AWBM)
Approach
  Divides catchment into three zones/area with similar hydraulic properties
  Assigns a storage capacity to each zone
  When storage capacity is exceeded, water is discharged to baseflow and surface flow stores
  These stores release flow according to the calibration coefficients assigned.
Inputs
  Daily precipitation (PrecipGen), or free water (snowmelt + rain) estimates from snow model (CemaNeige)
  Daily potential evapotranspiration (PET) (Hamon)
  Catchment Area
Calibration Parameters
  Baseflow Index (fraction of water that becomes baseflow)
  Surface runoff recession coefficient (Ks)
  Baseflow recession constant (Kb)
  Areas of catchment zones
  Storage capacity for each zone
The Australian Water Balance Model, Broughton, W., 2004 Environmental modeling and Software, Volume 19, Issue 10, PP 943-956
Surface Stores with different hydraulic characteristics
Storm hydrograph

## Slide 12: Catchment Runoff calibration

## Slide 13: Reservoir management
Inflows
  Precipitation
  Catchment runoff
Outflows
  Evaporation
  Managed releases (pool/allocator)
  Spills
Results
  Downstream Flows
  Fulfilment of irrigation demands
  Recreational releases

## Slide 14: Reservoir calibration
Downstream Flow Calibration
Reservoir Water Level Calibration

## Slide 15: Climate change
Climate change is modeled in General Circulation Models (GCMs)
GCMs represent alternative Shared Socioeconomic Pathways (SSPs)
There are 10s of GCMs, each with many alternative futures
Models investigate potential changes in CO2 levels on the planet based on possible futures associated with fossil fuel use, carbon sequestration efficiency etc. Results are in units of Watts/m2.
Results can be customized to specific locations
Dave Hoekstra, SRK, highlighted the challenges of extracting relevant results from Global Climate Change Models.

## Slide 16: Climate change – goldsim representation
  Colorado Models
  Colorado selected GCMs CMIP3 and CMIP5 for initial statewide assessment in 2012. (CMIP6 has been reviewed and found to be similar).
  Some state-specific calibration was performed
Preprocessing for Project-Specific Climate Change Data (Page Weil, LRE Water)
  40 years of synthetic daily data for 2050 for each of based on the selected models
  Each of the years represents 2050
  GoldSim uses the 25th, median and 75th percentile for inputs to climate scenarios.
Use in GoldSim Model
  Futures were calibrated in PrecipGen and TempGen
    Same methodology as the ‘no climate change’ calibration/forecast.
  After the end of the calibration period, all results represent a version of the climate in 2050. There is no ramp-up from 2024 to 2050.

## Slide 17: Scenario manager
Calibrated PrecipGen models for each climate scenario

## Slide 18: Climate change – RESULTS
Mean Annual Climate in 2050, 100 realizations
(Ignore the time scale! It’s all 2050)
Precipitation
Max Temperature
Historical Data
Climate Alternatives - 2050
Historical Data
Climate Alternatives - 2050
Historical Data
Climate Alternatives - 2050
Historical Data
Climate Alternatives - 2050
Pond Evaporation
Higher precipitation and evaporation
Higher maximum temperatures
Lower minimum temperatures
Min Temperature

## Slide 19: Climate scenario results
Climate Alternatives – 2050
Increased catchment runoff
Larger SEASONAL fluctuations in reservoir elevation
Downstream flowrates maintained
Historical Data
Climate Alternatives - 2050
Spillway Elevation
Monthly Downstream Flow Rates
Example Monthly 2050 Reservoir Water Elevations Predictions
Annual Catchment Runoff
Mean results representing 2050, 100 realizations
(Ignore the time scale! It’s all 2050)

## Slide 20: GOOD NEWS for fishing, Farming and boating IN 2050!
Predicted Monthly Recreational Flow Releases - 2050
Climate Alternatives - 2050

## Slide 21: Thanks TO: Page Weil (LRE Water): Concepts, input data and background on climate change modeling. Jason Lillywhite (GTG): Support for implementation of climate modeling tools in the GoldSim library, presentation title, and patience with getting me up to speed! Questions?
21

## Slide 22
LREWATER.COM