## Slide 1
Date: September 11, 2024
Presenter: Sunil Mehta
GoldSim User Conference 2024
Overview of GoldSim Based Modeling Applications to Support Environmental Decisions at the Hanford Site, Washington, USA

## Slide 2: Hanford Site, Washington
Established in 1943 as part of the Manhattan Project. Plutonium production took place from 1943 to 1989.
  Site occupies 580 square miles (1,518 km2) bordering Columbia River
During Cold War the project expanded to include 9 nuclear reactors and additional fuel processing/separations plants
450 billion gallons of liquids discharged to soil and large amount of solid waste generated
In 1989, site mission changed from production to clean-up
  Landmark agreement between U.S. Department of Energy, U.S. Environmental Protection Agency, and Washington State (known as the Tri-Party Agreement)
U.S DOE is responsible for one of the largest cleanup efforts in the world, managing the legacy of five decades of nuclear weapons production
225 miles

## Slide 3: Hanford Site: Waste Storage and Disposal
Waste generated from processing of 110,000 tons of irradiated uranium fuel from reactors
56 million gallons of radioactive waste stored in 177 large underground tanks
Large waste disposal facilities exist to support site mission
Environmental Restoration Disposal Facility

## Slide 4: Contamination in Vadose Zone and Saturated Zone

## Slide 5: Clean-up under Tri-Party Agreement (TPA)
Establishes goals for achieving full regulatory compliance and remediation with enforceable milestones
The TPA is a legally binding agreement for achieving compliance under federal
  CERCLA (Comprehensive Environmental Response Compensation and Liability Act) remedial action provision, and
  RCRA (Resource Conservation and Recovery Act) treatment, storage, and disposal regulations and correction action provision

## Slide 6: Example 1: Modeling Plumes in Regional Aquifer
To support baseline risk assessment the future concentration of contaminants had to be estimated in the regional aquifer that is outside the domain of the 3-D Model
Flow-paths are over 10 km long
GoldSim (ver. 10) based Pipe Pathways were used
  Uses a Laplace transform approach to provide analytical solution to advective-dominated mass transport system
  1-D transport model developed

## Slide 7: Example 1: Modeling Plumes in Regional Aquifer
Three Pipe Pathways deemed adequate based on flow paths
Each Pipe Pathway discretized into six segments to represent variations in saturated thickness and hydraulic conductivity
Upgradient boundary water flux and contaminant mass flux applied

## Slide 8: Example 1: Evaluation of Adequacy of 1-D Transport Model
Three segments of the Pipe Pathway shown along with inferred flow path
Applied boundary concentration based on Well 699-31-31 to the Pipe Pathway
Over 40 years of monitoring data
Chart: Time (years) from 1962
1
2
3
2.7 km
4.2 km
4.1 km

## Slide 9: Example 1: Evaluation of Adequacy of 1-D Transport Model
1
2
3
Chart: Time (years) from 1962
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
Model: 1st Pipe Segment | 0 | 4.0508e-07 | 0.018294 | 65.282 | 3687.9 | 36849 | 151180 | 369790 | 653640 | 933880 | 1156700 | 1297700 | 1357600 | 1354500 | 1313600 | 1259200 | 1208500 | 1166200 | 1127100 | 1084600 | 1035800 | 979550 | 911990 | 829250 | 731550 | 624760 | 517990 | 419470 | 334120 | 263010 | 204460 | 156130 | 116490 | 84839 | 60741 | 43778 | 33547 | 29071 | 28107 | 28012 | 27226 | 25538 | 23301 | 20846 | 18189 | 15266 | 12273 | 9469.7 | 7087.2 | 5266.1 | 3988.7
Model: 2nd Pipe Segment | 0 | 3.6869e-16 | 8.3421e-12 | 3.9731e-08 | 0.00020105 | 0.024377 | 0.83962 | 12.027 | 90.69 | 431.89 | 1464.6 | 3844.6 | 8294.9 | 15373 | 25294 | 37873 | 52597 | 68761 | 85617 | 102500 | 118890 | 134430 | 148860 | 162010 | 173760 | 183990 | 192600 | 199480 | 204510 | 207600 | 208720 | 207890 | 205200 | 200850 | 195020 | 187960 | 179910 | 171110 | 161770 | 152110 | 142330 | 132590 | 123050 | 113810 | 104970 | 96565 | 88637 | 81196 | 74240 | 67760 | 61741
Model: 3rd Pipe Segment | 0 | 4.1774e-21 | 2.3565e-16 | 1.0425e-12 | 6.9863e-09 | 1.4733e-06 | 0.00011651 | 0.0042589 | 0.07517 | 0.75772 | 4.9799 | 23.457 | 84.849 | 248.25 | 611.46 | 1308.2 | 2492.5 | 4313.1 | 6888 | 10284 | 14506 | 19504 | 25178 | 31397 | 38015 | 44880 | 51846 | 58774 | 65538 | 72019 | 78109 | 83709 | 88726 | 93082 | 96712 | 99569 | 101630 | 102880 | 103340 | 103040 | 102040 | 100390 | 98153 | 95417 | 92258 | 88757 | 84992 | 81036 | 76957 | 72816 | 68664
1
2
3

## Slide 10: Example 2: Performance Assessment (PA) of Radioactive Waste Disposal Facilities at Hanford
System model developed to integrate all subsystems of a disposal system
Identify the key parameters/processes important to performance and safety
System Model using GoldSim
3D Process Model
Inventory
Source Release
Inadvertent Intrusion Dose Computation
Groundwater Pathway (1D)
Air Pathway
Dose and Risk Computations
Groundwater Pathway (Process Model)
Abstraction of Flow Field

## Slide 11: Example 2: PA of Radioactive Waste Disposal Facilities
GoldSim features used:
  Source element, Cell pathway, Aquifer pathway
  Sorption and solubility limited release
  Diffusive and advective release
  Plume function to simulate effects of plume comingling in aquifer
  Cloning
  Stochastic elements
  Multivariate analysis
  Scenario and sensitivity analysis
3D process model for 21 trenches
1D system model
(cloned to 21 trenches)
Abstraction

## Slide 12: Example 2: PA of Radioactive Waste Disposal Facilities
A recent analysis involved 140+ nonzero uncertain parameters representing the important safety functions in the disposal system
300 realization simulation

## Slide 13: Example 3: Reactive Transport Modeling of Special Uranium Waste
Unirradiated uranium fuel rods, a significant source of uranium and technetium-99, are disposed in near surface landfill at the Hanford Site
  ~824 metric tons of uranium (~687 Ci)
Tc-99 exists as impurity within matrix of uranium metal (of about 10 ppm) ~140 Ci
Reactive transport modeling conducted to simulate dissolution of uranium and release of Tc-99 from this source
Effects of grout also incorporated
Scaled conceptual model implemented in GoldSim

## Slide 14: Example 3: Reactive Transport Modeling of Special Uranium Waste
Diffusive transport is the primary mechanism for contaminant migration to the surrounding soil
Flow accounted for in vertical and horizontal directions in the surrounding soil

## Slide 15: Example 3: Reactive Transport Modeling of Special Uranium Waste
GoldSim and PhreeqcRM coupling performed via a DLL
PhreeqcRM is a geochemical reaction module designed specifically to perform equilibrium and kinetic reaction calculations for reactive transport simulators that use an operator-splitting approach
GoldSim Cell Pathways are used to perform solute transport calculations and provide species concentration at each model cell at the end of a time step
The concentrations are passed to PhreeqcRM for geochemical reactions and are passed back to GoldSim Cell Pathways to be used at the start of the next time step
Calculations are performed seamlessly at all grid nodes (cells) and in distributed mode as well

## Slide 16: Example 3: Reactive Transport Modeling of Special Uranium Waste
(UO2)2SiO4·2H2O
UO3(TcO4H)0.0000242:2H2O
U billet Tc-99 release rate

## Slide 17: Example 4: Determination of Soil Concentrations Protective of Groundwater
Preliminary Remediation Goals (PRGs) represent the maximum quantity of analyte that can remain in soil without causing exceedance of applicable drinking water standards.
WQS=water quality standard, CI= initial concentration, CPK=peak groundwater concentration

## Slide 18: Example 4: Determination of Soil Concentrations Protective of Groundwater
Utilizes existing large scale (multi-million node) 3-D models to abstract representative flow fields under imposed recharge rates in the vadose zone
Transport in the future is primarily in vertical direction (1-D)
GoldSim is computationally efficient
  Multiple analytes can be modeled simultaneously
  20 chemicals and 7 radionuclides for current application
  Sorption and solubility controls

## Slide 19: Example 4: Determination of Soil Concentrations Protective of Groundwater
17 individual representative columns developed to capture the variability in vadose zone thickness and composition
Flow-fields abstracted from 3-D models.
Benchmark 1-D representative scenario transport against 3-D model transport
Simulate contaminant transport in 1-D representative scenarios

## Slide 20: Example 5: Hanford Soil Inventory Model (SIM)
The Hanford Soil Inventory Model (SIM) is a comprehensive tool designed to estimate the quantity and distribution of radionuclides and hazardous chemicals discharged to soil at the Hanford site
It provides critical information for site-wide applications
GoldSim is at the core
Hanford 200 Area Site Distribution for Tc-99

## Slide 21: Example 5: Hanford Soil Inventory Model (SIM)
Key functionalities include:
  Aggregating and processing large datasets to model site inventory over time.
    452 Waste Disposal Sites
    214 Waste Streams
    32 Chemicals, 47 Radionuclides
    Calculation from 1944 - 2001
  Propagates uncertainty by sampling uncertainty distributions of various inputs within looping containers
  Primary calculations performed using Array Constructor functions in a powerful manner (ability of arrays to reference variables as arguments)
Output site inventory mean and standard deviation over time
Inventory mean and variance calculations
Calculate mean and variance for density and concentration
Read all density and concentration input
Calculate mean and variance of site volumes
Read site volume input
Back decay site inventory data to discharge dates
SIM CALCULATION APPROACH
Loop over sites
Loop over times
Submodel Element Looped per Operable Unit (groups of sites)

## Slide 22: Example 5: Hanford Soil Inventory Model (SIM)
Script element: used for Uncertainty propagation and for back-decay calculations.

## Slide 23: Example 5: Hanford Soil Inventory Model (SIM)
The figure to the right shows the top 10 total chromium inventory sites for the 200 West Area at Hanford
The SIM, powered by GoldSim, has been instrumental in providing quantitative input for
  Fate and transport models
  Supporting decision-making for waste management and environmental protection.

## Slide 24: Concluding Remarks
Decisions related to Hanford Site clean-up and waste disposal activities require a variety of complex environmental modeling tasks
GoldSim modeling software has been used effectively over the past 15 years to support such environmental decisions
Examples highlight a wide range of GoldSim based applications that have received regulatory approval
Such modeling tasks will be required over next several decades to meet the TPA milestones