## Slide 1: Supporting Arizona Water Management in an Era of Limits Ken Seasholes Manager, Resource Planning & Analysis Central Arizona Project
New
^

## Slide 2: Arizona Water in the News
The Water Crisis Comes Home to Roost in Arizona
  Planetizen, February 6, 2023
Skipped Showers, Paper Plates: An Arizona Suburb’s Water Is Cut Off
  New York Times, January 16, 2023
“Phoenix is not so much a city as it is a monument to man's arrogance. It should not exist…”
  Anonymous comment posted on New York Times story
Arizona is running out of water. Big Tech data centers are partly to blame
  Business Insider, June 30, 2023
Arizona dries up as long-term drought and megafarms deplete scarce water resources
  The National, November 16, 2023
Arizona restricts Phoenix home construction amid water shortage
  Reuters, June 1, 2023

## Slide 3: Physical Setting
80% of the population (6.1M) lives in three counties
  Pima, Pinal & Maricopa
MARICOPA
PINAL
PIMA

## Slide 4: Physical Setting
Salt & Verde
River Watershed
Salt River Project Lands
80% of the population (6.1M) lives in three counties
  Pima, Pinal & Maricopa
Three major water supplies
  Surface water

## Slide 5: Physical Setting
Plateau Uplands
Central Highlands
High Productivity
Basin & Range
Lowlands
80% of the population (6.1M) lives in three counties
  Pima, Pinal & Maricopa
Three major water supplies
  Surface water
  Groundwater

## Slide 6: Physical Setting
Central
Arizona
Project
80% of the population (6.1M) lives in three counties
  Pima, Pinal & Maricopa
Three major water supplies
  Surface water
  Groundwater
  Colorado River water

## Slide 7: New Challenges
Colorado River: reservoirs at critically low elevations, and new rules for reservoir operations, including deeper reductions, must be negotiated
Groundwater: new restrictions on the use of groundwater to satisfy the State’s 100-year Assured Water Supply Rules for growth

## Slide 8: 3 Questions | 3 Scales | 3 Models
Who bears the burden of near-term Colorado River reductions?
  Basin Scale
What long-term water supplies will the Phoenix region need?
  Regional Scale
How much groundwater replenishment will residential subdivisions require?
  Neighborhood Scale

## Slide 9: Basin Scale: Colorado River Reductions
In June of 2022, Reclamation issued dire warnings about reservoir levels and pressed for large additional reductions through 2026
State negotiators made progress, but failed to reach a seven-state consensus
Regardless, Reclamation had to consider Alternatives as part of a Supplemental Environmental Impact Statement (SEIS)

## Slide 10: SEIS Scenario Model
To evaluate reduction concepts under consideration, CAP developed a small GoldSim model
  Takes output from Reclamation’s mid-term forecast model (CRMMS)
  Includes a basic dashboard with selectable policy options
  Visualizations in Excel

## Slide 11: SEIS Scenario Model
Within 24 hours of Reclamation releasing its draft SEIS, CAP’s model results were presented to the CAP Board of Directors
The key graphics were also posted on social media, circulated widely among stakeholders, and…

## Slide 12: SEIS Scenario Model
“…could I get copy of the Comparison of Alternatives chart that Senator Kelly wants to use on the Senate floor? He was hoping to get some modification to the graphics for easier read for the C-SPAN cameras…”
--Email from Senator Mark Kelly’s legislative staff
…put into the hands of national policymakers.

## Slide 13: Regional Scale: Demand for New Supplies
To address sedimentation and better capture flood flows, Salt River Project is proposing to raise one of its dams by 97 feet
  ~91,000 AF of yield
The economic evaluation needs to consider the demand for water supplies in the Phoenix region for the next 75+ years
  Reclamation reached out to CAP to assist by using the CAP Service Area Model (CAP:SAM)

## Slide 14: CAP:SAM
  Simulates the response of 130+ entities (cities, irrigation districts, tribes, etc.) to a wide range of supply and demand conditions
  Considers legal and regulatory framework
  Used for three Reclamation-funded “Basin Studies” in Arizona
  Extensive stakeholder engagement has lent credibility to the model
A complex model with an established track-record

## Slide 15: CAP:SAM
Making projections over such long periods required model modifications, and many heroic assumptions
  Growth modeling was adapted from EPA’s Integrated Climate and Land Use Scenarios (ICLUS) through the year 2100
  Stochastic CAP supply (modified random walk), bounded by plausible range of reductions, and climate change

## Slide 16: CAP:SAM
The CAP:SAM results suggest the long-term demand for new water supplies is potentially large, but may grow more gradually than some have speculated
The model provides an analytically robust framework for exploring options and alternatives

## Slide 17: Neighborhood Scale: Replenishment
CAP has responsibility for replenishing groundwater used by 1,300+ residential subdivisions that are “Member Lands”
  165,000 currently constructed homes
  100,000 additional unconstructed lots
Constructed Lots
Unconstructed Lots
MARICOPA
COUNTY
PINAL COUNTY
PIMA COUNTY
PHOENIX AMA
PINAL AMA
TUCSON AMA
PINAL COUNTY
MARICOPA
COUNTY
For regulatory purposes, CAP must project the replenishment required for all of the lots over the next 20+ years

## Slide 18: MeLO Model
The Member Land Obligation model (MeLO) was developed in GoldSim to simulate the physical and legal water use of each of the 1,300 subdivisions
  Key variables include rates of growth, supplies available to the provider, and contractual reporting requirements
ECs
ApplyECs

## Slide 19: MeLO Model
Water use at the household/parcel level is collected annually and helps inform model projections
19
Some Turf
Bare Ground; Rental
Pool; Turf Front & Back
Turf Front & Back; Kids
?
B-Ball Court;
Teens?

## Slide 20: MeLO Model
MeLO was developed as part of process to submit a statutorily required “Plan of Operation” to the Arizona Department of Water Resources

## Slide 21: Model Comparisons
Model Name | Entities Simulated | Model Elements | Container levels | Outputs
SEIS | 31 | 217 | 2 | 2,087
CAP:SAM | 140 | 2,055 | 5 | 440,090
MeLO | 1,331 | 173 | 2 | 618,938

## Slide 22: CAP’s GS Modeling Approach
CAP’s policy models are organized around processes and computational steps
  GS’s visual environment is used to illuminate the mechanics of the model
  Limit equation complexity
    Break into smaller steps
  Show all ins & outs
    Expression Elements are repurposed with custom icons
  Containerize
    At higher levels: processes/systems
    At deeper levels: emphasize the math
  Use consistent style and naming conventions
    e.g., prefixes, CamelCase, verbose names, etc.

## Slide 23: A parting thought…
Arizona’s water managers are faced with growing challenges and difficult choices. Ultimately, these are not going to be resolved with more data or better models, but planning & analysis can help.
So stay tuned…

## Slide 24: A parting thought…
Arizona’s water managers are faced with growing challenges and difficult choices. Ultimately, these are not going to be resolved with more data or better models, but planning & analysis can help.
So stay tuned…